## Slide 1: NJDEP Division of Air Enforcement
NJ State Police Training Center, Robbinsville, NJ
May 4, 2016
Diesel Enforcement Program
Regulatory Review, Green Trucks, TRUs
Graphics in this presentation have been sourced from the internet and are royalty and copyright free to the best of my knowledge.
Presented by – Ralph Bitter, Supervisor, Diesel Enforcement
ACE Academy
New Jersey Department of Environmental Protection

## Slide 2
>3
“Idling”
Running the engine without propelling the motor vehicle.
Idling for more than 3 minutes is prohibited, with some exceptions.
N.J.A.C.
7:27-14
Diesel-powered
Motor
Vehicles
N.J.A.C.
7:27-15
Gasoline-powered
Motor
Vehicles

## Slide 3
“Diesel/gasoline-powered”
means utilizing a diesel or gasoline engine.
“Gasoline” includes:
gasoline, natural gas,
Liquefied petroleum gas, propane,
alcohol, fuel blends AND hydrogen!

## Slide 4
“Motor vehicle” means all vehicles propelled otherwise than by muscular power…
to Hell

## Slide 5
…excepting motorized bicycles and such vehicles as run only upon rails or tracks.

## Slide 6
Federal Preemption – no enforcement on locomotives

## Slide 7
Federal Preemption

## Slide 9
Idling can burn up to one gallon per hour!
…and wastes natural resources.
Exhaust fumes are TOXIC!
WHY ?!

## Slide 10: NJDEP Division of Air Enforcement
Diesel Enforcement Program
“Green Label” Trucks

## Slide 11
USEPA approved technologies - includes idling limiters.
“Green Label” Trucks
CA NOx limit at idle – OR 5 minute auto-shutoff.
Unlimited use – if the main engine is shut off.

## Slide 12: NJDEP Division of Air Enforcement
Diesel Enforcement Program
Transport Refrigeration Units (TRU)

## Slide 13
Transportation refrigeration units (TRUs) are gasoline and diesel powered cooling units that are installed on vehicles used to transport produce, meat, dairy products, and other perishable goods. TRUs are found on refrigerated vans, trucks, trailers, railcars, and shipping containers.
Transport Refrigeration Units (TRU)
The TRU gasoline or diesel engines drive either mechanical or electric compressors. Sometimes an APU is utilized to power the trailer in transit. Some TRUs are equipped with electric standby systems (ESS), which allow them to use “shore-power” – electricity provided by the facility where they are housed.

## Slide 14
Vehicle mounted:
Alternator and direct belt drive – drive engine dependent
Auxiliary diesel and APU – a modular unit utilizing the vehicles fuel tank
Self contained
  may have their own fuel supply or tap into the vehicles fuel tank
  may have electric standby systems (ESS) to use “shore-power”
Trailer (Reefer) mounted:
Self contained
  have their own fuel supply and exhaust system
  may have electric standby systems (E/S) to use “shore-power
Containers:
Self contained
  have their own fuel supply and exhaust system
  have electric standby systems (ESS) to use “shore-power
TRU Systems

## Slide 15
Alternator and direct belt drive:
drive engine dependent
Typically roof-mounted
Light duty vehicles
Idling exempt when in use
Vehicle Mounted Systems
Auxilliary Diesel and APUs:
Engine on-board
Typically frame-mounted
Utilizes the vehicles fuel
Medium to heavy-duty vehicles
Idling exempt

## Slide 16
Typical roof-mount – exempt.

## Slide 17
May be plug-in.
Look for fuel tank tap.

## Slide 18
Likely just an insulated box, but the refrigeration unit may be inside. Likely electric - check for connections.

## Slide 19
Self contained:
  Body or frame-mounted
  Medium to heavy-duty vehicles
  Typically may have their own fuel supply, some tap into the vehicles fuel tank
  may have electric standby systems (ESS) to use “shore-power”
  Vehicle NOT idling exempt
Vehicle Mounted Systems

## Slide 20
Self-Contained Units
This may be a frame mounted fuel tank.

## Slide 21
Note shore-power connection and frame-mounted tank

## Slide 22
TRU Fuel Tank

## Slide 23
Guard rails are an indicator for TRU tanks.
Note the frame-mounted tank behind the rail.

## Slide 24
Demountable truck/trailer bodies

## Slide 25
Shore-power line
Evaporator drains
Umbilical with fuel line – look for connection to the trucks fuel tank
Commonly mounted on trucks, sometimes a frame trailer.
The truck is NOT exempt.
Self-contained TRU – Frame mounted body

## Slide 26
Trailer-Mounted Units
Self contained:
  body or frame-mounted
  have their own fuel supply
  may have electric standby systems (EES) to use “shore-power”
  Tractor NOT idling exempt

## Slide 27
A typical long-haul refrigerated reefer.
TRU Fuel Tank
TRU

## Slide 28
TRU Tank behind landing gear.

## Slide 30
A portable cold storage container.
The tractor is NOT exempt when it’s being transported.
Shipping Containers

## Slide 31
Built-in TRU container

## Slide 32
1. Access Panel (Evap. Fan #1) 9. Supply Temperature Supply/Recorder Sensor Assembly (STS/SRS)
2. Fork Lift Pockets 10. Economizer
3. Control Box 11. Ambient Temperature Sensor (AMBS)
4. Unit Display 12. Power Cables and Plug (Location)
5. Key Pad 13. Autotransformer
6. Remote Monitoring Receptacle 14. Condenser Grille
7. Start−Stop Switch, ST 15. Upper Fresh Air Makeup Vent Panel (Evap. Fan #2)
8. Compressor
Refrigeration Unit - Front Section

## Slide 33
Modal chassis mount
Integrated TRU
Under chassis TRU

## Slide 34
Checklist
Dedicated fuel tank
Self contained or separate power source - not the vehicles engine
Tap to vehicle fuel tank
Ask:
Does the vehicle engine have to be running for the A/C to work?

## Slide 35
Is the vehicle exempt?

## Slide 36
Critics Choice
We don’t care as long as it stays cold!

## Slide 37: For more information:
Ralph Bitter, Supervisor
Diesel Enforcement
609-292-6429
ralph.bitter@dep.nj.gov