## Slide 1: Pharmaceutical Rule, Generator Improvement Rule, eManifest, & Biennial Reporting
Prepared by: Bret Reburn
Environmental Specialist 3
Hazardous Waste Enforcement
Central Regional Office - Trenton, NJ
(609) 292-3949
bret.reburn@dep.nj.gov

## Slide 2: Hazardous Waste Pharmaceuticals (Proposed Rule)
Adapted from USEPA presentation

## Slide 3: Link to Phamaceutical Rule
http://www.gpo.gov/fdsys/pkg/FR-2015-09-25/pdf/2015-23167.pdf

## Slide 4: Clarifying Guidance
Epinephrine salts not Acute P-listed wastes
  RCRA Online memo #14778; dated October 15, 2007
Residues in partially-used syringes are not listed wastes
  RCRA Online memo #14788; dated April 14, 2008
Nicotine patches, gum, lozenges are P-listed when unused
  RCRA Online memo #14817; dated August 23, 2010

## Slide 5: Clarifying Guidance (continued)
Limited fix for containers with P-listed pharmaceutical residues
  RCRA Online memo #14827; dated November 4, 2011
Phentermine salts are not P-listed wastes
  RCRA Online memo #14831; dated February 17, 2012
Household pharmaceuticals collected during take-back events should be incinerated
  RCRA Online memo #14833; dated September 26, 2012

## Slide 6: Clarifying Guidance (continued)
E-cigarettes are P075
  RCRA Online memo #14850; dated May 8, 2015
Nicotine-containing smoking cessation products are not solid wastes (or HW) when sent for nicotine reclamation
  RCRA Online memo #14851; dated May 8, 2015

## Slide 7: Overview of Proposed Rule
Proposing sector-specific rules for the management of hazardous waste pharmaceuticals for:
  Healthcare facilities/pharmacies
  Reverse distributors

## Slide 8: Overview (continued)
Two flows:
  Creditable hazardous waste pharmaceuticals that go through reverse distribution to obtain manufacturer’s credit
  Non-creditable hazardous waste pharmaceuticals that do not and should not go through reverse distribution

## Slide 9: Where are the Regulations?
40 C.F.R. 266
Currently under Part 266:
  Subpart F – Precious Metals
  Subpart G – Batteries
  Subpart M – Military Munitions
  New:
  Subpart P - Management Standards for Hazardous Waste Pharmaceuticals

## Slide 10: Who Will be Covered?
Healthcare facilities that generate hazardous waste pharmaceuticals
Does not include healthcare facilities that are CESQGs
All pharmaceutical reverse distributors - regardless of current generator category

## Slide 11: Proposed Definition of Healthcare Facility
Any person that :
  provides preventative, diagnostic, therapeutic, rehabilitative, maintenance or palliative care, and counseling, service, assessment or procedure with respect to the physical or mental condition, or functional status, of a human or animal or that affects the structure or function of the human or animal body; or
  sells or dispenses over-the-counter or prescription pharmaceuticals.

## Slide 12: Healthcare Facility
lncludes (but is not limited to):
  Hospitals, including psychiatric hospitals
  Pharmacies, including
    Long-term care pharmacies
    Mail-order pharmacies
    Retail stores with pharmacies
  Health clinics

## Slide 13: Healthcare Facility
(continued)
  Surgical centers
  Long-term care facilities
  Physicians offices, including dental, optical, & chiropractors
  Veterinary clinics and hospitals
  Drug compounding facilities
  Coroners & medical examiners
Drug manufacturers are not considered healthcare facilities

## Slide 14: Proposed Definition of Reverse Distributor
  Any person that receives and accumulates potentially creditable hazardous waste pharmaceuticals for the purpose of facilitating or verifying manufacturer’s credit

## Slide 15: Proposed Definition of Reverse Distributor
  Any person, including forward distributors and pharmaceutical manufacturers, that processes pharmaceuticals for the facilitation or verification of manufacturer’s credit is considered a pharmaceutical reverse distributor

## Slide 16: Sewering Pharmaceuticals
Rule proposes ban on sewering of HW pharmaceuticals
Sewer ban applies to all healthcare facilities & RDs, including CESQGs
At EPA’s urging DEA no longer allows sewering as a means of destroying controlled substances

## Slide 17: Containers with Residues
If residues are acute/P-listed HW, then to be considered “RCRA empty,” containers must be:
  Triple-rinsed, or
  Cleaned by another method shown in the scientific literature or by tests by generator, to achieve equivalent removal

## Slide 18: Containers with Residues
Residues in unit-dose containers and dispensing bottles/vials would be exempt from RCRA
  Unit-dose containers (e.g., packets, cups, wrappers, blister packs and unit-dose delivery devices) and
  Dispensing bottles and vials up to 1 liter or 1000 pills

## Slide 19: Containers with Residues
If all contents are removed equivalent to “RCRA empty”
Container may be disposed of as non-hazardous waste
Original packaging, including dispensing vials & bottles, must be destroyed to prevent diversion

## Slide 20: Containers with Residues
Dispensed syringes exempt if:
  Syringe used to administer the pharmaceutical to a patient
  Syringe is placed in a sharps container that is managed appropriately
EPA seeking comment on quantity limits

## Slide 21: Containers with Residues
All other containers, including delivery devices, that once held listed or characteristic pharmaceuticals, must be managed as hazardous waste:
  IV bags and tubing
  Inhalers
  Aerosols
  Nebulizers
  Tubes of ointment, gels, creams

## Slide 22: DEA & EPA Intersection
RCRA Wastes also DEA controlled:
  Chloral hydrate (U034)
  Fentanyl sublingual spray (D001)
  Phenobarbital (D001)
  Testosterone gels (D001)
  Valium injectable (D001)
These are dually regulated by EPA and DEA – must comply with both sets of regulations

## Slide 23: DEA & EPA Intersection
Conditional Exemptions:
Hazardous waste pharmaceuticals that are also DEA controlled substances would be exempt from RCRA regulation
Conditions for exemption:
  Must be managed in accordance with all DEA regulations
  Must be combusted at permitted or interim status:
    municipal solid waste combustor
    hazardous waste combustor

## Slide 24: LQG Status Due to Acute HW
HW pharmaceuticals not counted toward healthcare facility’s generator status when managed under Part 266 Subpart P
  No SQG or LQG status for HW pharmaceuticals
  All HW pharmaceuticals are managed the same

## Slide 25: LQG Status Due to Acute HW
  Don’t need to keep track of monthly generation for hazardous waste pharmaceuticals
  Don’t need to accumulate acutes and non-acutes separately
  Reduces incidences of episodic generation

## Slide 26: Shipments Off-Site from a Healthcare Facility
Potentially Creditable HW pharmaceuticals can go to a Pharmaceutical Reverse Distributor:
  Written, advance notice of shipments
  Confirmation of receipt by RD
  Recordkeeping of shipments to RD
  Common carrier allowed
  HW codes not required during shipment

## Slide 27: Shipments Off-Site from a Healthcare Facility
Non-creditable HW pharmaceuticals must go to TSDF
  HW transporter required
  Manifesting required
  HW codes not required on manifest
  “Hazardous waste pharmaceuticals” in Box 14 of manifest

## Slide 28: Proposed definition “Potentially Creditable”
  Hazardous waste pharmaceutical that has the potential to receive manufacturer’s credit and is:
  Unused or un-administered
  Unexpired or less than one year past expiration date

## Slide 29: Proposed definition “Potentially Creditable”
  The term does not include:
    Evaluated hazardous waste pharmaceuticals
    Residues of pharmaceuticals remaining in containers
    Contaminated personal protective equipment, and
    Clean-up material from the spills of pharmaceuticals

## Slide 30: Not “Potentially Creditable”
Since manufacturers set the policies of when a pharmaceutical receives credit, a healthcare facility does not always know when credit will be given

## Slide 31: Not “Potentially Creditable”
No reasonable expectation of credit…cannot go to an RD, for example if the pharmaceutical:
  Is a sample
  Is a generic
  More than 1 year past expiration
  Been removed from original container and re-packaged
  Was generated during patient care, or refused by a patient

## Slide 32: What’s Ahead?
Proposed rule published in the Federal Register on 9/25/15
60-day public comment period ends 11/24/15
EPA reviews public comments
EPA commences work on final rule
EPA decides whether to proceed on additional proposed or final rules related to:
  Expanding what pharmaceuticals are hazardous
  Nicotine

## Slide 34: Hazardous Waste Generator Improvements (Proposed Rule)
Adapted from USEPA presentation

## Slide 35: Link to Generator Rule
http://www.gpo.gov/fdsys/pkg/FR-2015-09-25/pdf/2015-23166.pdf

## Slide 36: Goals of the Proposed Rule
  Reorganize to make them more user-friendly and improve compliance
  Provide greater flexibility for hazardous waste generators to manage waste in a cost-effective manner
  Strengthen environmental protection by addressing identified gaps in the regulations
  Clarify certain components of the hazardous waste generator program to address ambiguities and foster improved compliance

## Slide 37: Reorganization of Generator Regulations
Provision | Existing Citation | Proposed Citation
Generator Category Determination | § 261.5(c)(e) | § 262.13
CESQG Provisions | § 261.5(a), (b), (f)(g) | § 262.14
Satellite Accumulation Area Provisions | § 262.34(c) | § 262.15
SQG Provisions | § 262.34(d)(f) | § 262.16
LQG Provisions | § 262.34(a), (b), (g)(i), (m) | § 262.17

## Slide 38: CESQG Waste Consolidation
Consolidate waste at an LQG under the control of the same person:
  Person – as defined under RCRA
  Control – power to direct policies at the facility
  CESQG must marks/label waste containers with the words
  “VSQG Hazardous Waste”

## Slide 39: CESQG Waste Consolidation
  LQG must:
  Notify state on Site ID Form about participation in activity and identify CESQGs participating
  Keep records for each shipment
  Manage consolidated waste as LQG hazardous waste
  Submit a Biennial Report

## Slide 40: Episodic Generation
Allow generators to maintain existing category provided they comply with streamlined set of requirements:
  One event per calendar year
  May petition for second event
  Notify EPA or state prior to initiating a planned event
  Complete event and ship waste off-site within 45 days (30-day extension possible)

## Slide 41: Episodic Generation
Streamlined Requirements for CESQGs:
  Obtain EPA ID Number
  Use hazardous waste manifest and transporter to send episodic waste to TSDF or recycler
  Manage the episodic hazardous waste in a manner that minimizes the possibility of an accident or release

## Slide 42: Episodic Generation
CESQG requirements continued:
  Label episodic waste containers
  Identify emergency coordinator
  Maintain records
SQGs:
Need only comply with existing SQG regulations and maintain records associated with the episodic event

## Slide 43: Preparedness and Planning
Problem
Contingency plans are submitted to local’s but are lengthy
Emergency responders want quick access to important information
Proposed Solution
Require new LQGs submitting plans to include an executive summary that has the most critical information

## Slide 44: Preparedness and Planning
Contents of Executive Summary:
  Types & amounts of hazardous waste
  Maps of site and of surrounding area
  Location of water supply
  Identification of notification systems (telephones, PA)
  Emergency contact

## Slide 45: Hazardous Waste Determinations
Require SQGs & LQGs to keep documentation when solid waste is found to be non-hazardous
  Would focus only on solid wastes found in 40 CFR 261.2 (i.e., spent materials, sludges etc.) that have potential to be a listed or characteristically hazardous

## Slide 46: Labeling
Must indicate hazards contents
Must have “plain English” words that identify container contents
Indicate hazards of contents using any of several established methods
Tanks, drip pads, containment buildings can keep this information in logs or records kept near the accumulation site

## Slide 47: Re-notification by SQGs
Problem
EPA/States have outdated and inaccurate databases of SQG universe
No requirement to notify periodically
Difficult to plan or execute inspections as effectively
Proposed Solution
Require SQGs to re-notify every 2 years
Electronic reporting option

## Slide 48: Biennial Reporting
LQGs must report all hazardous waste generated in a calendar year, even when it is managed the next calendar year
LQGs must report hazardous wastes generated throughout calendar year, even for months when they are an SQG
Recycling facilities must report wastes that are not stored prior to recycling

## Slide 49: Satellite Accumulation Areas
Require that hazardous wastes not be mixed or placed in a container with other hazardous wastes that are incompatible
Allow containers to remain open under limited circumstances, when necessary for safe operations
Provide maximum weight in addition to volume for acute hazardous waste limit

## Slide 50: Satellite Accumulation Areas
Clarify that “three days” means three calendar days
Explain that when maximum weight or volume is exceeded, waste must be moved to a central accumulation area or TSDF
Rescind memo allowing reactive hazardous waste to be stored away from the point of generation

## Slide 51: Waiver of 50-Foot Requirement
Allow the generators to approach the fire department to apply for a waiver from the requirement if the fire department believes that the precautions taken by the facility make the waiver appropriate and safe.

## Slide 52: Closure
Require closure as a landfill for when LQGs accumulating in containers fail to clean close
Require LQGs to notify EPA or authorized state no later than 30 days prior to closing an accumulation area and within 90 days after closure of unit or facility

## Slide 53: What’s Ahead?
Proposed rule published in the Federal Register on 9/25/15
60-day public comment period ends 11/24/15
EPA reviews public comments and commences work on final rule
Effective date/State adoption & authorization

## Slide 55: E-MANIFEST

## Slide 56: E-Manifest
“Hazardous Waste Electronic Manifest Establishment Act” signed 10/5/12
EPA to implement national electronic manifest system (E-Manifest)
Final rule signed on 2/7/14
System running by 10/5/15
EPA not allowing use of eManifest as of today

## Slide 57: WEBLINKS
EPA Main Manifest page: http://www2.epa.gov/hwgenerators/hazardous-waste-manifest-system
eManifest page: http://www3.epa.gov/epawaste/hazard/transportation/manifest/e-man.htm
Final rule:
http://www.gpo.gov/fdsys/pkg/FR-2014-02-07/pdf/2014-01352.pdf

## Slide 59: BIENNIAL REPORTS

## Slide 60: BIENNIAL REPORT INFO:
Submitted in even numbered years for previous (odd) years generation
Provides EPA/States a summary of haz. waste generation/management

## Slide 61: BIENNIAL REPORT INFO:
Helps EPA measure compliance with regulations & waste minimization
Is summarized/communicated to the public through the National Biennial RCRA Hazardous Waste Report

## Slide 62: WHO IS REQUIRED TO SUBMIT BIENNIAL REPORTS?
Facilities that were LQG’s during previous (odd-numbered) year
Facilities that treated, stored, or disposed of RCRA hazardous wastes on-site during previous (odd-numbered) year

## Slide 63: WHERE TO SUBMIT REPORT:
Submit electronically
American Resource Management, Inc. (ARM) http://www.arminc.net
Hard copies are accepted but processing fees are much higher

## Slide 64: FOR MORE INFORMATION :
http://www.epa.gov/wastes/inforesources/data/biennialreport/

## Slide 65: MAILING ADDRESS MANIFEST UNIT
NJDEP
Haz. Waste/UST Comp. & Enf.
9 Ewing Street
Mail Code 09-03
P.O. Box 420
Trenton, NJ 08625-0420
Attn: Manifest Unit