# RFQ

# NJDOT Truck Wash Facility Maintenance

# Four (4) Locations Throughout New Jersey

# STATE OF NEW JERSEY

# Honorable Chris Christie, Governor

Honorable Kim Guadagno, Lt. Governor

# DEPARTMENT OF TRANSPORTATION

# Richard T. Hammer, Commissioner

Date: October 27, 2016

Project:          NJDOT Truck Wash Facility Maintenance

Project Sites:  		NJDOT Headquarters

1035 Parkway Avenue

Ewing, NJ 08618

NJDOT Keasbey Repair Garage

90 Crows Mill Road

Keasbey, NJ 08832

NJDOT Vineland Repair Garage

1959 South Delsea Drive (Rt. 47)

Vineland, NJ 08360

NJDOT Wall Township Maintenance Facility

2436 Paynters Road

Wall Township, NJ 08736

Important Dates:

- Question Cut-Off:   Questions shall be submitted to the Procurement Contact below via e-mail no later than: Tuesday, November 1, 2016 @ 10:00 AM.

- Answers to Bid Questions:  Bidders are encouraged to monitor the website daily for updates, changes and responses to questions through the Bid Opening due date.

- Bid Opening:  Bid Quotes, including mandatory DPA Forms, must be submitted to the Procurement Contact below via e-mail no later than:

Thursday, November 3, 2016 @ 10:00 AM

Procurement Contact:	Viktoriya Usachenok:  609-530-2418

viktoriya.usachenok@dot.nj.gov

State Contract Manager:    	George Schwartz:  609-530-2878

## 1.1 PURPOSE AND INTENT

This Request for Quotation (RFQ) is issued by the New Jersey Department of Transportation (NJDOT).  The purpose of this RFQ is to solicit proposals for monthly inspection and preventive maintenance of truck washing facilities throughout the State of New Jersey for a term period beginning on November 1, 2016 and ending March 31, 2017.  Additionally, a fixed hourly rate for service calls and a discount percentage for parts are also being solicited. The following are the service locations:

- NJDOT Headquarters

1035 Parkway Avenue

Ewing, NJ 08618

- NJDOT Keasbey Repair Garage

90 Crows Mill Rd.

Keasbey, NJ 08832

- NJDOT Vineland Repair Garage

1959 South Delsea Dr. (Rt. 47)

Vineland, NJ 08360

- NJDOT Wall Township Maintenance Facility

2436 Paynters Road

Wall Township, NJ 08736

## 1.2 BACKGROUND

This is a short term contract from November 1, 2016 through March 31, 2017 to ensure that the NJDOT facilities are properly maintained and operational at all times.  A general overview of the monthly inspection and preventive maintenance as follows:

Preventative maintenance is to be performed on a routine schedule identified and detailed in the Scope of Work within this RFP.

## 2.0 SCOPE OF WORK

INSPECTION AND MAINTENANCE

Inspection and maintenance work shall be performed on a monthly, scheduled basis.

Maintenance is to be limited to normally expendable items such as grease, filters, belts, activated carbon, filter sand/media, pH strips, indicator lights and the like.

Equipment, tools, materials and all other items required to perform the inspection and maintenance work shall be provided by the Contractor and shall include, but not be limited to hand tools, power tools, pumps, ladders, drums, buckets, containers, rags, wipes, gloves, spill absorbent, safety equipment, lifts, hoists, cranes, vacuum trucks, etc.

All inspection and maintenance work shall be performed in accordance with OSHA requirements, the NJDOT General Health and Safety Requirements and all other applicable health and safety requirements.

After any periodic inspection, preventative maintenance or service call repair site visit, any equipment, tools, materials, etc. which may have been provided by the contractor for the performance of the service shall be taken off-site by the Contractor.  Any tools, equipment, materials, etc. stored on the job site is at the risk of the Contractor.

After any periodic inspection, preventative maintenance or service call repair site visit, any waste such as boxes, wraps, shipping material, containers, spent rags, debris, wastewater, waste oil, sludge, etc, which may have been generated by or associated with the service shall be properly disposed of off-site by the Contractor.

Removed parts are to be shown to the NJDOT Contract Manager prior to being properly discarded off-site by the contractor.  The NJDOT Contract Manager will initial the Field Service Report verifying the description and quantity of the parts replaced.  Failure to obtain this verification may result in a delay in the processing of the Contractor’s invoice or the invoice being returned.

Inspection and maintenance work is to be performed during regular State working hours (Monday through Friday, 7:30 a.m. to 4:00 p.m.), except State holidays.

The inspection and maintenance work is defined as being performed on straight time and shall include, but not be limited, to the tasks indicted in the following Inspection and Maintenance Schedule:

## NJDOT HQ MONTHLY INSPECTION AND MAINTENANCE (FIVE (5) VISITS)

1035 Parkway Avenue

Ewing, NJ 08618

(Equipment to be inspected, maintained and/or repaired includes:  Whiting Smartwash Equipment, Carbtrol Washwater Recycling System, Power Washer - Alhota Cleaning Systems Model 4201 NG, Air Compressor – Speedaire Model 1WD80, Air Dyer - Hankinson Model HIT20 and Backflow Preventers - ¾” Watts Model 009-M3 QT and 2” Watts Model LF009M2QT)

WHITING SMARTWASH EQUIPMENT

Check spray nozzles on all three spray arches; remove and clean nozzles as necessary.

Check level of soap tank.

Check pumps, valves and piping in the wash bay and equipment room for leaks.

Clean wash bay floor and equipment room of loose debris and trash.

Check belts on spinner arch for correct tension and adjust, if necessary.

Clean photo eye lenses if necessary.

Check spinner assemblies and adjust if necessary.

Check spinner drive belts for tears.

Check rotating spinner unions for water leaks.

Check air cylinders for leaks and proper operation.

Grease rotating unions on spinner arch – 13 unions total.

AIR COMPRESSOR

Drain moisture from tank.

Clean dust and foreign matter from cylinder head, motor, fan blade, air lines, intercooler and tank.

Check v-belts for tightness.  Adjust as necessary.

VEHICLE DRYER FANS

Check fans for any debris or obstructions.

Check all bolts for tightness.

Check fans and welds for damage, cracks or fractures.

POWER WASHER

Check unit for proper operation.

Check belt for tightness.

WASH WATER RECYCLING SYSTEM

Remove sludge and scum from clarifier.

Backwash filters.

Check ozone system run light.

Clean manifold strainer.

Check pH and dissolved solids of recycled water.

Remove oil from knock down pits with oil skimmer provided by NJDOT.

Check chemical feed pump to verify operation and delivery of hydrogen peroxide to the system.

Check level of the drum of hydrogen peroxide.

AIR DRYER

Inspect the condenser coils.  Remove accumulated dust and dirt with a soft brush or with air from an OSHA approved compressed air nozzle that limits the discharge pressure to 30 psig.

## KEASBEY MONTHLY INSPECTION AND MAINTENANCE (FIVE (5) VISITS)

90 Crows Mill Road

Keasbey, NJ 08832

(Equipment to be inspected, maintained and/or repaired includes: Oil Trap ElectroPulse Water Treatment System, Zurn Proceptor Oil-Water Separator and Power Washer -Hotsy Model 991A)

WATER TREATMENT (OIL TRAP) SYSTEM

Clean glass bulb of pH probe.

Check pH for proper level with pH strips.

Inspect and/or clean pre-screen in sump tank.

Check proper pumping of chemical pumps.

Check sludge level in sludge tank and change dewatering bag if required.

Check sludge level in knock down pit.

Check electro-cell and replace if required.

Check levels in the brine, polymer and sanitizer tanks and create new solutions if required.

Check proper pump operation.

POWER WASHER

Check unit for proper operation.

Check belt for tightness.

OIL-WATER SEPARATOR

Check level of oil and sediment

## VINELAND MONTHLY INSPECTION AND MAINTENANCE (FIVE (5) VISITS)

1959 South Delsea Drive (Rt. 47)

Vineland, NJ 08360

(Equipment to be inspected, maintained and/or repaired includes: Oil Trap ElectroPulse Water Treatment System and Power Washer – Hotsy Model 982SS)

WATER TREATMENT (OIL TRAP) SYSTEM

Clean glass bulb of pH probe.

Check pH for proper level with pH strips.

Inspect and/or clean pre-screen in sump tank.

Check proper pumping of chemical pumps.

Check sludge level in sludge tank and change dewatering bag if required.

Check sludge level in knock down pit.

Check electro-cell and replace if required.

Check levels in the brine, polymer and sanitizer tanks and create new solutions if required.

Check proper pump operation.

POWER WASHER

Check unit for proper operation.

Check belt for tightness.

## WALL MONTHLY INSPECTION AND MAINTENANCE (FIVE (5) VISITS)

2436 Paynters Road

Wall Township, NJ 08736

(Equipment to be inspected, maintained and/or repaired includes: Carbtrol Wash Water Recycling System, Power Washer – Hotsy Model 942N and Backflow Preventer - 2” Watts Model LF009M2QT)

WASH WATER RECYCLING SYSTEM

Remove sludge and scum from clarifier.

Backwash filters.

Check ozone system run light.

Clean manifold strainer.

Check pH and dissolve solids of recycled water.

Check chemical feed pump to verify operation and delivery of hydrogen peroxide to the system.

Check level of the drum of hydrogen peroxide.

Remove oil from the knock down pits with oil skimmer provided by NJDOT.

POWER WASHER

Check unit for proper operation.

Check belt and insure proper tightness.

COORDINATION OF EQUIPMENT SHUT DOWN AT ANY LOCATION

If equipment must be shut down for service or repairs, the Contractor is required to coordinate the schedule with the designated representative at the site or the NJDOT Contract Manager before any shutdown.

REIMBURSEMENT OF REPAIR PARTS

Replacement and repair of parts as well as complete devices are a part of this contract. Bidders are encouraged to provide a discount off parts. Bidders are reminded that the State may, at its discretion, provide the required repair parts. Reimbursement will be made only with the submission of supplier's invoice.  All shipping costs are considered to be part of the overall cost. The NJDOT reserves the right to request the Contractor to obtain competitive pricing for materials.  Bidders are reminded that an audit of their supply invoices and all other documents may be undertaken not only during the contract period, but also upon completion of the contract for a period of five (5) years. The contractor shall have available the type of inventory required to service and repair all systems.

SERVICE CALLS

Service calls include service that requires a response and action within sixteen (16) hours of notification by the designated representative at the site or the State Contract Manager. A list of these persons will be provided to the contractor. This service shall be conducted during State working hours during the business next day after notification. The Contractor must have the ability to be notified at all times through the use of a 24-hour emergency service telephone number.

In order to meet this response time, a local office must be within a seventy-five (75) mile radius of the contract site.

The Contractor responding to these service calls shall remain on the job site until the truck wash facility is placed back into normal operation.  In the event that repair and/or replacement parts are needed and not readily available to place the truck wash facility back into normal operation, the Contractor shall not leave the job site until the facility is shut down and is safe.  In this case the Contractor shall immediately notify the designated representative at the site or the NJDOT Contract Manager of the nature and reason that the truck wash facility could not be repaired along with a scheduled return visit to make the required repairs.  A fixed hourly rate shall be submitted for these calls.

EMPLOYEE STATUS

The Contractor shall use trained technicians supervised by the Contractor.  These technicians shall be properly qualified to keep all equipment included in this proposal properly maintained and operating.  The State Contract Manager reserves the right to reject technicians.

GENERAL CONDITIONS

The Contractor shall furnish a written work slip upon completion of all ongoing service calls detailing all work performed and the parts replaced or repaired.  To ensure system continuity, replacement parts and devices offered must be standard equipment, compatible with existing components and installed in accordance with the manufacturer’s recommendations. No software or wiring changes will be permitted to modify the existing systems unless authorized by the State Contract Manager. The Contractor’s work slip will be used against every invoice to verify all payments. Failure to adhere to this requirement could result in forfeiture of payment for services rendered. In the event a technician cannot be provided on the requested day, notification must be given to the NJDOT Contract Manager. If the normally assigned technician is not available, the approved backup technician must be provided. The work site is to be left in a clean and orderly condition. The Contractor shall be available for additional work over and above the scope of the agreement.  The Contractor shall not proceed with any additional work without written permission from the State and shall complete work as expediently as possible after receiving approval. All invoices submitted by the Contractor shall be itemized clearly indicating the breakdown of labor in hours, number of crew and the parts used.

CONTRACTOR PERSONNEL PHOTO IDENTIFICATION

Upon entering and/or leaving any location(s) which shall be serviced for this contract, all contractor personnel and any subcontractor personnel must be able to provide a photo ID.

Contractor's personnel and any subcontractor personnel shall display laminated picture identification on their person. The identification shall clearly display the individual's first and last names printed in block letters underneath the picture. The contractor's logo or subcontractor logo shall also appear on the picture side of the card. The individual's identification number (not social security number) and signature shall be included on the back of the identification card. Any contractor's or subcontractor's employee reporting to work without company identification badge will not be permitted to enter the building.

CONTRACTOR PERSONNEL UNIFORM REQUIREMENTS

Contractor's personnel assigned to State facilities shall wear a uniform supplied by the contractor bearing the contractor's logo or other company identification. The company's name must be visible at all times. Any contractor's employee reporting to work without uniform will not be permitted to remain in the building. This provision is also applicable to any subcontractor's personnel.

WARRANTY

All inspection and service calls are to be guaranteed to be free of all mechanical and electrical system shut downs for a period of five (5) calendar days from the date of the visit.  Should the system malfunction or become inoperable within the five (5) day period, NJDOT will only pay for parts.  There will be no additional charges for travel, labor or the service call in order to get the system back to 100% performance.

In the event that the Contractor returns to the site to install a part or to perform an additional service which could not be accomplished during the previous inspection or service call, the State will pay for both parts and labor provided the return visit is not associated with a malfunction of a previous repair that occurs during the five (5) day warranty period.  No other additional service call charges will be paid under any circumstances.

All parts, components, systems and equipment that require replacement due to the preventative maintenance or service call repair work are to be covered by the manufacturer’s standard warranty and warranty period.  This warranty period shall be explicitly stated in the Field Service Report that is submitted as required in this Scope of Work.

REPLACEMENT OF UNSATISFACTORY ITEMS

In the event that the item(s) supplied, in the opinion of the NJDOT, is not providing satisfactory performance or requires and excessive amount of remedial maintenance and the item(s) is still under warranty, the Contractor, after notice in writing by the NJDOT that such a situation exists, agrees to remove and replace the defective component within ten (10) days of such notice at no cost to the NJDOT.

# NJDOT Truck Wash Facility Maintenance

BID PROPOSAL FORM TO BE SUBMITTED WITH BIDDER’S RESPONSE

The bid quote is to be submitted to the buyer via the e-mail noted in the RFQ, and will be accepted no later than 10:00 AM on Thursday, November 3, 2016.

FIRM NAME

AND ADDRESS:

(Please type or print)

| LINE# | DESCRIPTION/MFGR/BRAND | EST QUANTITY | UNIT | UNIT PRICE | TOTAL PRICE |
| --- | --- | --- | --- | --- | --- |
| 1 | PRICE FOR MONTHLY INSPECTION AND MAINTENANCE (FIVE (5) VISITS) NJDOT HEADQUARTERS 1035 PARKWAY AVENUE EWING, NJ 08618 | 5 | MO | $______EA | $___________ |
| LINE# | DESCRIPTION/MFGR/BRAND | EST QUANTITY | UNIT | UNIT PRICE | TOTAL PRICE |
| 2 | PRICE FOR MONTHLY INSPECTION AND MAINTENANCE (FIVE (5) VISITS) NJDOT KEASBEY REPAIR GARAGE 90 CROWS MILL ROAD KEASBEY, NJ 08832 | 5 | MO | $______EA | $___________ |
| LINE# | DESCRIPTION/MFGR/BRAND | EST QUANTITY | UNIT | UNIT PRICE | TOTAL PRICE |
| 3 | PRICE FOR MONTHLY INSPECTION AND MAINTENANCE (FIVE (5) VISITS) NJDOT VINELAND REPAIR GARAGE 1959 SOUTH DELSEA DRIVE (RT. 47) VINELAND, NJ 08360 | 5 | MO | $______EA | $___________ |
| LINE# | DESCRIPTION/MFGR/BRAND | EST QUANTITY | UNIT | UNIT PRICE | TOTAL PRICE |
| 4 | PRICE FOR MONTHLY INSPECTION AND MAINTENANCE (FIVE (5) VISITS) NJDOT WALL TOWNSHIP MAINTENANCE FACILITY 2436 PAYNTERS ROAD WALL TOWNSHIP, NJ 08736 | 5 | MO | $______EA | $___________ |
| LINE# | DESCRIPTION/MFGR/BRAND | EST QUANTITY | UNIT | UNIT PRICE | TOTAL PRICE |
| 5 | FIXED HOURLY RATE FOR SERVICE CALLS | 1 | HOUR | $______HR | $___________ |
| LINE# | DESCRIPTION/MFGR/BRAND | EST QUANTITY | UNIT | % DISCOUNT | TOTAL DISCOUNT |
| 6 | REPAIR PARTS AND SUPPLIES - DISCOUNT FROM CONTRACTOR’S CATALOG ENTER CATALOG DATE: __________________ | 1 | PCT | ______% | __________% |

NOTE:

DPA Forms must be submitted with the Bid Proposal Form for your submission to be valid.  Failure to submit the DPA Forms may deem your quote non-responsive.

Line #5: The Bidder must submit an all-inclusive fixed hourly price to include, but not limited to direct labor, overhead, fee or profit, clerical support, managerial (administrative) support, all documents, reports, forms, travel, reproduction and any other associated costs.  No additional fees or costs shall be paid by the State unless there is a change in the scope.

# Text boxes

ID#: