## Slide 1
New Jersey Department of Environmental Protection
Transportation Oversight Unit
Bob Gomez, Supervisor
Ron Feehan, Lawrence Lewis, Chris Farrar
& Mike Kosierowski
9 Ewing Street, Mail Code 09-01
P.O. Box 420
Trenton, New Jersey 08625-0420
(609) 292-6305

## Slide 2: Responsibilities Of TOU
Solid, Hazardous & Medical Waste Transporter Compliance
10-Day HW Transfer Facility Inspections
  Load consolidation, check DOT markings, packaging & compatibility
  Record keeping – log books, (DOT & RCRA requirements) hazardous waste manifests (shipping descriptions & emergency contact #)
  Vehicle Compliance Inspections
    Generator locations where waste is offered for transport
    Roadside with NJSP
    10-Day HW Transfer Facilities
    Disposal Facilities

## Slide 3: Selecting A Transporter
Do I use a waste broker or find my own transporter?
Brokers & transporters require an A-901 license (HW & SW)
  Solid waste transporters & brokers also require CPCN
  HW & SW transporters are also required to be registered with DEP to transport the type of waste they are transporting and are issued decals to place on their equipment

## Slide 4: Selecting A Transporter
  Reputable transporter or broker checklist:
  Always ask for copy of A-901 & CPCN (for SW)
  Is equipment displaying current decals (look at equipment)
  Check DOT Safer site to make sure the transporter has not been revoked by DOT & to check compliance & safety ratings
  Check NJ DEP’s Data Miner to evaluate compliance history

## Slide 5: Various Types of DEP Decals

## Slide 6: A-901 License & CPCN Examples

## Slide 7: DOT Requirements Applicable to Hazardous Waste Generator’s
  Comply with training requirements
  Properly identify waste being shipped
  Select an authorized package
  Properly mark the package
    EPA & DOT marking requirements
  Complete the shipping paper (HW Manifest)
  Comply with placarding requirements

## Slide 8: DOT Requirements Applicable to Hazardous Waste Generator’s
  Training (49 CFR 172.704)
    Hazmat employers must provide training to their hazmat employees & shall include:
      General awareness training - enabling the employee to recognize & identify hazardous materials

## Slide 9: DOT Requirements Applicable to Hazardous Waste Generator’s
  Training 172.704 - cont.
    Function Specific – hazmat employee must receive specific training to the hazmat function(s) performed
    Safety training – shall include emergency response information, methods of avoiding accidents such as proper handling procedures, & measures to protect themselves from exposure

## Slide 10: DOT Requirements Applicable to Hazardous Waste Generator’s
  Training 172.704 - cont.
    Security awareness & In-depth security training
      Refer to Subpart I (172.800 & 172.804) for security plan specifics
    Initial & recurrent training
      Initial completed within 90 days of hire or change in function, may work under direct supervision of knowledgeable hazmat employee until training is completed
      Recurrent must be done at least every 3 years
      Relevant training received from a previous employer or other
      source is also acceptable
Notes: Security Awareness must be provided to all hazmat employees - it must include:
-- awareness of security risks associated with hazmat transportation
--methods designed to enhance transportation security
--it must also include a component covering how to recognize & respond to possible security threats.

## Slide 11: DOT Requirements Applicable to Hazardous Waste Generator’s
  Training 172.704 - cont.
      Training Records Must Include:
      Hazmat employee's name
      Completion date of most recent training
      Training Materials (Copy, description, or location)
      Name and address of hazmat trainer
      Certification that the hazmat employee has been trained and tested
Notes: Security Awareness must be provided to all hazmat employees - it must include:
-- awareness of security risks associated with hazmat transportation
--methods designed to enhance transportation security
--it must also include a component covering how to recognize & respond to possible security threats.

## Slide 12: Identify Your Waste
Generator knowledge (MSDS, prior analytical)
Testing of waste material
  EPA & DOT have very detailed testing methodology protocols

## Slide 13: Examples of Basic Descriptions
    Acetone, 3, UN1090, PGII
    Phosphoric acid solution, 8, UN1805, PGIII
    On January 1, 2013, the sequence was altered to
    match the international sequence:
    1. UN ID number
    2. Proper shipping name
    3. Hazard class
    4. Packing group
    Now the basic description for these chemicals
    is:
    UN1090, Acetone, 3, PGII
    UN1805, Phosphoric acid solution, 8, PGIII

## Slide 14: Shipping Paper – HW Manifest

## Slide 15: Uniform Hazardous Waste Manifest is the Shipping Paper For Hazardous Waste
  Select basic shipping description from the 172.101 Table by:
      Selecting proper shipping name (PSN)
      Hazard Class
      ID number
      Packing Group
      Total quantity being shipped
      If the PSN does not include the word “waste” & hazardous waste is being shipped the word waste must precede the proper shipping name

## Slide 16: Uniform Hazardous Waste Manifest is the Shipping Paper For Hazardous Waste
  Shipping Paper Cont.
      Provide Emergency Response Information
        (E.R.G. # or MSDS form)
      Emergency Response Telephone number, see 172.604
        Monitored at all times the material is in transportation (until it is accepted at TSD)
        Person must have knowledge of material being shipped & have comprehensive ER information of the material or immediate access to someone who has this knowledge.

## Slide 17: Uniform Hazardous Waste Manifest is the Shipping Paper For Hazardous Waste
  Shipping Paper Cont.
      Generator Certification 172.204
        By signing the manifest the generator is certifying the consignment is fully & accurately described by the proper shipping name, classified, packaged, marked, labeled, & in all respects in proper condition for transport...

## Slide 18: DOT Requirements Applicable to Hazardous Waste Generator’s
  General Non-Bulk Marking Requirements 172.301
    For hazardous waste EPA marking required at 40 CFR 262.32 must be on package & include:
      Generator’s name & address, manifest document #, proper shipping description, technical names, special permit #
    Other prescribed DOT markings shall be used, where required, such as package orientation arrows for liquids, inhalation hazard, marine pollutant for vessel transportation (where applicable), or Biohazard

## Slide 19: DOT Non Bulk Package Marking
DOT Hazard Warning Labels:
      Same surface of package and near PSN
      Primary & subsidiary labels, when required, must be next to each other (within 6 inches of each other)

## Slide 20: DOT Non Bulk Package Markings
Types of Markings:
  EPA Marking
  DOT Hazard Warning Labels
  Package Orientation Arrows
Notes: Non bulk packages have a max. cap. Less than:
- For Liquids <119 gallons (450 liters)
- For Solids <882 pounds (400 kilograms)
- For Gas <1,000 pounds (454 kilograms)
Bulk packages anything greater than non-bulk quantity.

## Slide 21: Improper Packaging
Result of lithium
batteries that were not
packaged properly

## Slide 22: Properly Packaged & In Proper Condition for Transportation?

## Slide 23: Properly Packaged & In Proper Condition for Transportation?
Must make sure package is closed in accordance with closure instructions
In this case a plastic bung was used in place of a metal one

## Slide 24: Properly Packaged & In Proper Condition for Transportation?
Bung was not tightened
Does not meet the minimum packaging standard at 49 CFR 173.24

## Slide 25: Placarding
General rules:
  Must appear on all four faces of the tractor/trailer
  Required for:
    Bulk packaging regardless of quantity
    Table 1 – Any quantity
    Table 2 – Equals or exceeds 1001 lbs. or 454 Kg in non-bulk packaging or any quantity in bulk packaging
    Joint responsibility of shipper and carrier
49 CFR 172.500

## Slide 26: Placarding
Notes: Non bulk ID marking
- when 4,000 kg (8,820 lbs.) or more is picked up at an individual location
Bulk package ID# marking
- all 4 sides for packages with >1,000 cap. Or more
- on 2 opposing sides for bulk packages <1,000 gal. Cap.

## Slide 27: DOT Requirements Applicable to Hazardous Waste Generator’s
  Labeling Requirements - Subpart E
    Label(s) selection, Column 6 of 172.101 Table
    Label placement on package 172.406
      Same surface of package and near PSN
      Primary & subsidiary labels, when required, must be next to each other (within 6 inches of each other)
      As of 10/1/05, all subsidiary labels must contain a hazard class or division number in the lower corner

## Slide 28: DOT Requirements Applicable to Hazardous Waste Generator’s
  Placarding Requirements - Subpart F
    Placard selection, Column 3 of 172.101 Table
    Generator’s responsibility 172.506
      Each person offering a motor carrier a hazardous material for transportation by highway shall provide to the motor carrier the required placards for the material being offered prior to or at the same time the material is offered for transportation, unless the carrier’s motor vehicle is already placarded for the material as required by this subpart

## Slide 29: DEP Vehicle Marking Requirements

## Slide 30: Helpful Web Links
US DOT Pipeline & Hazardous Materials Safety Administration
http://www.phmsa.dot.gov/hazmat
Regulations
Interpretations
Training resources
Regional DOT contact information
US DOT Hazardous Materials Information Center
800-467-4922 or phmsa.hm-infocenter@dot.gov
US DOT Federal Motor Carrier Safety Administration
https://safer.fmcsa.dot.gov/CompanySnapshot.aspx
Quick look at compliance & safety ratings of a transporter

## Slide 31: Helpful Web Links
NJ DEP Transporter Registration Page
http://www.nj.gov/dep/dshw/hwr/regislic/lru.htm
Go to drop down menu and select type of transporter you are looking for:
  Report – Solid Waste Transporters (A-901 Licensed)
  Hazardous Waste Transporters (A-901 Licensed)
  Medical Waste Transporters
  NJ DEP Transporter Compliance History via Data Miner
  http://www.nj.gov/dep/opra/online.html
  Click on blue button on right “click here to launch DEP Data Miner”
  Search by name of transporter. For questions navigating Data Miner contact Liz Hennessey at (609) 292-6305 or elizabeth.hennessey@dep.nj.gov

## Slide 32: TOU Contacts & Areas of Knowledge
Bob Gomez, Supervisor (609) 292-3837 robert.gomez@dep.nj.gov
Areas of knowledge: RCRA, DOT, A-901 and Solid & Hazardous Waste Transportation
Ron Feehan, Investigator (609) 292-3853 ron.feehan@dep.nj.gov
Areas of knowledge: Solid Waste Transportation, A-901 and Utility Regulations
Mike Kosierowski, Env. Specialist 3 (609) 439-9640 michael.kosierowski@dep.nj.gov
Areas of knowledge: RCRA, DOT and Solid & Hazardous Waste Transportation
Lawrence Lewis, Env. Specialist 2 (609) 209-1762 lawrence.lewis@dep.nj.gov
Areas of knowledge: Solid, Hazardous and Medical Waste Transportation
Chris Farrar, Env. Specialist 1 (609) 439-8217 chris.farrar@dep.nj.gov
Area of knowledge: Solid Waste Transportation