## Slide 1: Radiation and Radioactivity
Radiation: Energy in transit, either particulate or electromagnetic in nature
Radioactivity: The characteristic of various materials to emit ionizing radiation
Ionization: The removal of electrons from an atom. The essential characteristic of high energy radiations when interacting with matter.
Notes: Radiation is energy traveling in the form of particles or waves in bundles of energy called photons. Some everyday examples are microwaves used to cook food, radio waves for radio and television, light, and x-rays used in medicine.
Demonstration with Chart of Electromagnetic Spectrum
Radioactivity is a natural and spontaneous process by which the unstable atoms of an element emit or radiate excess energy in the form of particles or waves. These emissions are collectively called ionizing radiations. Depending on how the nucleus loses this excess energy either a lower energy atom of the same form will result, or a completely different nucleus and atom can be formed.
Demonstration of Chart of Nuclides with Next Slide
Ionization is a particular characteristic of the radiation produced when radioactive elements decay. These radiations are of such high energy that when they interact with materials, they can remove electrons from the atoms in the material. This effect is the reason why ionizing radiation is hazardous to health, and provides the means by which radiation can be detected.

## Slide 2: The Atom
<footer>
<date/time>
Protons 11p
(1.007276 amu)
Neutrons 10n
(1.008665 amu)
Electrons
(0.0005486 amu)
Neon-20 2010Ne
(19.992434 amu)
Notes: A typical model of the atom is called the Bohr Model, in honor of Niels Bohr who proposed the structure in 1913. The Bohr atom consists of a central nucleus composed of neutrons and protons, which is surrounded by electrons which “orbit” around the nucleus.
Protons carry a positive charge of one and have a mass of about 1 atomic mass unit or amu (1 amu =1.7e10-27 kg, a very, very small number). Neutrons are electrically “neutral” and also have a mass of about 1 amu. In contrast electron carry a negative charge and have mass of only 0.00055 amu.
The number of protons in a nucleus determines the element of the atom. For example, the number of protons in uranium is 92 and the number in neon is 10. The proton number is often referred to as Z. Atoms in nature are electrically neutral so the number of electrons orbiting the nucleus equals the number of protons in the nucleus.
Neutrons make up the remaining mass of the nucleus and provide a means to “glue” the protons in place. Without neutrons, the nucleus would split apart because the positive protons would repel each other. Elements can have nucleii with different numbers of neutrons in them. For example hydrogen, which normally only has one proton in the nucleus, can have a neutron added to its nucleus to from deuterium, ir have two neutrons added to create tritium, which is radioactive. Atoms of the same element which vary in neutron number are called isotopes. Some elements have many stable isotopes (tin has 10) while others have only one or two. We express isotopes with the nomenclature Neon-20 or 2010N, with twenty representing the total number of neutrons and protons in the atom, often referred to as A, and 10 representing the number of protons (Z).

## Slide 3: Alpha Decay
Alpha Particle
(Helium Nucleus)
(4.00147 amu)
Parent Nucleus
Am-241
U-238
Th-232
Ra-226
Daughter
Nucleus
Np-237
Th-234
Ra-228
Rn-222
  
Notes: Alpha decay is a radioactive process in which a particle with two neutrons and two protons is ejected from the nucleus of a radioactive atom. The particle is identical to the nucleus of a helium atom.
Alpha decay only occurs in very heavy elements such as uranium, thorium and radium. The nucleii of these atoms are very “neutron rich” (i.e. have a lot more neutrons in their nucleus than they do protons) which makes emission of the alpha particle possible.
After an atom ejects an alpha particle, a new parent atom is formed which has two less neutrons and two less protons. Thus, when uranium-238 (which has a Z of 92) decays by alpha emission, thorium-234 is created (which has a Z of 90).
Because alpha particles contain two protons, they have a positive charge of two. Further, alpha particles are very heavy and very energetic compared to other common types of radiation. These characteristics allow alpha particles to interact readily with materials they encounter, including air, causing many ionizations in a very short distance. Typical alpha particles will travel no more than a few centimeters in air and are stopped by a sheet of paper.
Show decay on chart of nuclides,
Show smoke detector as application of alpha decay.

## Slide 4: Beta (Negatron) Decay


Parent Nucleus
Rhenium-187
Potassium-40
Daughter
Nucleus
Osmium-187
Calcium-40
Beta Particle
(electron)
Antineutrino
Notes: Beta decay is a radioactive process in which an electron is emitted from the nucleus of a radioactive atom, along with an unusual particle called an antineutrino. The neutrino is an almost massless particle that carries away some of the energy from the decay process. Because this electron is from the nucleus of the atom, it is called a beta particle to distinguish it from the electrons which orbit the atom.
Like alpha decay, beta decay occurs in isotopes which are “neutron rich” (i.e. have alot more neutrons in their nucleus than they do protons). Atoms which undergo beta decay are located below the line of stable elements on the chart of the nuclides, and are typically produced in nuclear reactors.
When a nucleus ejects a beta particle, one of the neutrons in the nucleus is transformed into a proton. Since the number of protons in the nucleus has changed, a new daughter atom is formed which has one less neutron but one more proton than the parent. For example, when rhenium-187 decays (which has a Z of 75) by beta decay, osmium-187 is created (which has a Z of 76).
Beta particles have a single negative charge and weigh only a small fraction of a neutron or proton. As a result, beta particles interact less readily with material than alpha particles. Depending on the beta particles energy (which depends on the radioactive atom), beta particles will travel upto several meters in air, and are stopped by thin layers of metal or plastic.
Show compact fluorescent light bulb as application of beta decay.

## Slide 5: Gamma-Ray Emission
Gamma Ray
Parent Nucleus
Cesium-137
Molybdenum-99
Daughter Nucleus
Barium-137m
Technetium-99m

Notes: After a decay reaction, the nucleus is often in an “excited” state. This means that the decay has resulted in producing a nucleus which still has excess energy to get rid of. Rather than emitting another beta or alpha particle, this energy is lost by emitting a pulse of electromagnetic radiation called a gamma ray. The gamma ray is identical in nature to light or microwaves, but of very high energy.
Like all forms of electromagnetic radiation, the gamma ray has no mass and no charge. Gamma rays interact with material by colliding with the electrons in the shells of atoms. They lose their energy slowly in material, being able to travel significant distances before stopping. Depending on their initial energy, gamma rays can travel from 1 to hundreds of meters in air and can easily go right through people.
It is important to note that most alpha and beta emitters also emit gamma rays as part of their decay process. However, their is no such thing as a “pure” gamma emitter.
Important gamma emitters including technetium-99m which is used in nuclear medicine, and cesium-137 which is used for calibration of nuclear instruments.

## Slide 6: Positron Decay
<footer>
<date/time>


Positron Particle
(Positive electron)
Neutrino
Daughter
Nucleus
Boron-11
Carbon-13
Parent Nucleus
Carbon-11
Nitrogen-13
+
-
Annihilation
Radiation
Notes: Positron decay is very similar to beta decay but instead of ejecting an electron, the nucleus ejects a positron and a neutrino. A positron is identical to an electron, but has positive instead of negative charge.
In contrast to alpha and beta decay, positron decay occurs in isotopes which are “neutron poor” (i.e. have less neutrons in their nucleii than stable forms of the element). Atoms which undergo positron decay are located above the line of stable elements on the chart of the nuclides, and are typically produced in cyclotrons.
When a nucleus ejects a positron particle, one of the protons in the nucleus is transformed into a neutron. Since the number of protons in the nucleus has changed, a new daughter atom is formed which has one less proton but one more neutron than the parent. For example, when carbon-11 decays (which has a Z of 6) by positron decay, boron-11 is created (which has a Z of 5).
Positron particles have a single positive charge and weigh the same as an electron. As a result, positrons and beta particles interact identically in material. However, positrons have a very short existence in this universe because as soon as they slow down and interact with a normal electron, the electron and positron will annihilate each other, releasing energy. This energy is in the form of two annihilation photons traveling in opposite directions. Each photon has the equivalent energy of an electron or positron according to the relationship E=mc2.
Positrons are the key ingredient to positron emission tomography.

## Slide 7: Electron Capture and Characteristic X-Rays
Characteristic X-Ray
Parent Atom
Cobalt-57
Daughter Nucleus
Iron-57

Neutrino
Notes: Electron capture is a decay process that can also take place in atoms that undergo positron decay. The nucleus, instead of ejecting a positron, absorbs one of the electrons which are orbiting the nucleus. When this occurs the electron combines with a proton to become a neutron. Since the net effect is to convert a proton to a neutron, the new daughter atom formed has one less proton but one more neutron than the parent. For example, when carbon-11 decays (which has a Z of 6) by electron capture, boron-11 is created (which has a Z of 5).
Electron capture like positron decay occurs in atoms which are neutron poor. These atoms are located above the line of stable elements on the chart of the nuclides, and are typically produced in cyclotrons.
When an electron is absorbed into the atom, a “hole” is created in the orbit of the electrons which surround the atom. Because this hole is lower in energy then most of the surrounding electrons, it is natural for one of the electrons in a higher orbit to fall into this hole and fill the vacancy. When this occurs energy is released in the form of a “characteristic x-ray”. An x-ray is another form of electromagnetic radiation, like light and radar waves, but of very high energy like gamma rays. The only difference between gamma rays and x-rays is that gamma rays come from the nucleus of an atom and x-rays come from the electron shell.
Electron capture is an important reaction in nuclear medicine.

## Slide 8: X-Ray Production (Bremsstrahlung)
Electron
X-Ray
Target Nucleus
Tungsten
Cathode
(-)
Anode (+)
X-Rays
Notes: Almost a century ago in 1895, Roentgen discovered the first example of ionizing radiation, x-rays. The key to Roentgens discovery was a device called a Crooke’s tube, which was a glass envelope under high vacuum, with a wire element at one end forming the cathode, and a heavy copper target at the other end forming the anode. When a high voltage was applied to the electrodes, electrons formed at the cathode would be pulled towards the anode and strike the copper with very high energy. Roentgen discovered that very penetrating radiations were produced from the anode, which he called x-rays.
X-ray production whenever electrons of high energy strike a heavy metal target, like tungsten or copper. When electrons hit this material, some of the electrons will approach the nucleus of the metal atoms where they are deflected because of there opposite charges (electrons are negative and the nucleus is positive, so the electrons are attracted to the nucleus). This deflection causes the energy of the electron to decrease, and this decrease in energy then results in forming an x-ray.
Medical x-ray machines in hospitals use the same principle as the Crooke’s Tube to produce x-rays. The most common x-ray machines use tungsten as there cathode, and have very precise electronics so the amount and energy of the x-ray produced is optimum for making images of bones and tissues in the body.

## Slide 9: Types of Radiation
Alpha



Beta
Gamma and X-rays
Neutron
Paper
Plastic
Lead
Concrete
10n
Notes: In summary, the most common types of radiation include alpha particles, beta and positron particles, gamma and x-rays, and neutrons.
Alpha particles are heavy and doubly charged which cause them to lose their energy very quickly in matter. They can be shielded by a sheet of paper or the surface layer of our skin. Alpha particles are only considered hazardous to a persons health if an alpha emitting material is ingested or inhaled.
Beta and positron particles are much smaller and only have one charge, which cause them to interact more slowly with material. They are effectively shielded by thin layers of metal or plastic and are again only considered hazardous if a beta emitter is ingested or inhaled.
Gamma emitters are associated with alpha, beta, and positron decay. X-Rays are produced either when electrons change orbits within an atom, or electrons from an external source are deflected around the nucleus of an atom. Both are forms of high energy electromagnetic radiation which interact lightly with matter. X-rays and gamma rays are best shielded by thick layers of lead or other dense material and are hazardous to people when they are external to the body.
Neutrons are neutral particles with approximately the same mass as a proton. Because they are neutral they react only weakly with material. They are an external hazard best shielded by thick layers of concrete. Neutron radiation will be discussed in more detail in the discussion of nuclear power.
Demonstration of alpha, beta, and gamma with fiesta plate and GM detector.

## Slide 10: Measures of Radioactivity
Activity: The quantity of radioactive material present at a given time:
  Curie (Ci) : 3.7x1010 disintegration per
  second (dps)
  milliCurie (mCi): 3.7x107 dps
  microCurie (mCi): 3.7x104 dps
  picoCuries (pCi): .037 dps
  Becquerel (Bq): 1 dps
  megaBecquerel (MBq): 1x106 dps
Specific Activity: The amount of radioactivity in a given mass or volume, e.g. pCi/l or Ci/gm
Notes: When given a certain amount of radioactive material, it is customary to refer to the quantity based on its activity rather than its mass. The activity is simply the number of disintegrations or transformations the quantity of material undergoes in a given period of time.
The two most common units of activity are the Curie and the Becqueral. The Curie is named after Pierre Currie for his and his wife Marie’s discovery of radium. One Curie is equal to 3.7x1010 disintegrations per second. A newer unit of activity if the Becqueral named for Henry Becquerel who is credited with the discovery of radioactivity. One Becqueral is equal to one disintegration per second.
It is obvious that the Curie is a very large amount of activity and the Bequeral is a very small amount. To make discussion of common amounts of radioactivity more convenient, we often talk in terms of milli and microCuries or kilo and MegaBecquerels.
When dealing with large amounts of material, either solids, liquids or gases, it is often convenient to talk about the activity in a given mass or volume of the material. This is called the specific activity of the material.

## Slide 11: Half-Life
The time required for the
amount of radioactive material
to decrease by one-half
Notes: Half-life is the time required for the quantity of a radioactive material to be reduced to one-half its original value.
All radionuclides have a particular half-life, some of which a very long, while other are extremely short. For example, uranium-238 has such a long half life, 4.5e109 years, that only a small fraction has decayed since the earth was formed. In contrast, carbon-11 has a half-life of only 20 minutes. Since this nuclide has medical applications, it has to be created where it is being used so that enough will be present to conduct medical studies.

## Slide 12: Radiation Detection Gas Filled Detectors
Air or Other Gas
Incident Ionizing Radiation
Electrical
Current
Measuring
Device
+
-
Cathode -
Anode +
+
+
+
-
-
-
+
-
Voltage Source
Notes: Since we cannot see, smell or taste radiation, we are dependent on instruments to indicate the presence of ionizing radiation.
The most common type of instrument is a gas filled radiation detector. This instrument works on the principle that as radiation passes through air or a specific gas, ionization of the molecules in the air occur. When a high voltage is placed between two areas of the gas filled space, the positive ions will be attracted to the negative side of the detector (the cathode) and the free electrons will travel to the positive side (the anode). These charges are collected by the anode and cathode which then form a very small current in the wires going to the detector. By placing a very sensitive current measuring device between the wires from the cathode and anode, the small current measured and displayed as a signal. The more radiation which enters the chamber, the more current displayed by the instrument.
Many types of gas-filled detectors exist, but the two most common are the ion chamber used for measuring large amounts of radiation and the Geiger-Muller or GM detector used to measure very small amounts of radiation.
Demonstration of Geiger-Muller Detector.

## Slide 13: Radiation Detection Scintillation Detectors
Incident Ionizing Radiation
Sodium-Iodide
Crystal
Photocathode
Optical Window
-
Pulse
Measuring
Device
Light Photon
Photomultiplier Tube
Dynode
Anode
Notes: The second most common type of radiation detecting instrument is the scintillation detector. The basic principle behind this instrument is the use of a special material which glows or “scintillates” when radiation interacts with it. The most common type of material is a type of salt called sodium-iodide. The light produced from the scintillation process is reflected through a clear window where it interacts with device called a photomultiplier tube.
The first part of the photomultiplier tube is made of another special material called a photocathode. The photocathode has the unique characteristic of producing electrons when light strikes its surface. These electrons are then pulled towards a series of plates called dynodes through the application of a positive high voltage. When electrons from the photocathode hit the first dynode, several electrons are produced for each initial electron hitting its surface. This “bunch” of electrons is then pulled towards the next dynode, where more electron “multiplication” occurs. The sequence continues until the last dynode is reached, where the electron pulse is now millions of times larger then it was at the beginning of the tube. At this point the electrons are collected by an anode at the end of the tube forming an electronic pulse. The pulse is then detected and displayed by a special instrument.
Scintillation detectors are very sensitive radiation instruments and are used for special environmental surveys and as laboratory instruments.
Demonstration of NaI detector

## Slide 14: Radiation and Radioactivity
Radiation: Energy in transit, either as particles or electromagnetic waves
Radioactivity: The characteristic of various materials to emit ionizing radiation
Ionization: The removal of electrons from an atom. The essential characteristic of high energy radiations when interacting with matter.

## Slide 15: Radiation Units
Roentgen: A unit for measuring the amount of gamma or X rays in air
Rad: A unit for measuring absorbed energy from radiation
Rem: A unit for measuring biological damage from radiation

## Slide 16: Elements
An element is the smallest amount of a substance that still exhibits the properties of that substance.
Elements are classified by the number of protons in each atom, and can be arranged in order in the Periodic Chart.

## Slide 17: Atoms
Atoms are the building blocks of all matter, made up of protons and neutrons and electrons.
Almost all atoms are very stable, but some may have too much energy and be radioactive.

## Slide 18: Molecules and Compounds
Atoms group together or bond to each other forming molecules and compounds.
Examples of these are water (2 hydrogen, 1 oxygen atoms) and sugar (6 carbon, 12 hydrogen and 6 oxygen atoms)

## Slide 19: Three States of Matter
Solid: Solids are items don't change their shapes like rocks, wood and ice.
Liquid: Liquids flow, like water, alcohol and glass
Gas: Gases are free flowing, like air, oxygen and steam.
The difference between each is the amount of energy the molecules have

## Slide 20: Electromagnetic Waves
Electromagnetic waves are energy waves, ranging from the low energy radio waves to the high energy gamma rays.
They have a height (amplitude) and a length between wave peaks (wave length)

## Slide 21: Non-Ionizing Electromagnetic Radiation
Non-Ionizing Electromagnetic Radiations do not have enough energy to remove electrons from atoms, such as:
  Ultraviolet Radiation
  Light
  Infrared Radiation
  Microwaves
  Radio Waves

## Slide 22: Contamination vs Radiation
Radiation and Contamination are often confused. Radiation is energy, while contamination is the physical presence of a radioactive material on something.
So, you may have contamination on your shoe, but not radiation.

## Slide 23: Ionizing Electromagnetic Radiation
Ionizing Electromagnetic Radiations do have enough energy to remove electrons from atoms, such as:
  X-rays
  Gamma rays

## Slide 24: Units of Contamination
Contamination, or the presence of radioactive material on something is measured as count on a detector per some time like a minute (cpm), or by the actual decay rate (dps).

## Slide 25: Radiation Effects and Risk
Exposure: A measure of ionization in air from x-ray and gamma rays.
  Roentgens, or mR
Dose: A measure of the energy absorbed in any material as a radiation passes through it.
  Rads or mrads, Gray or mGy.
Dose equivalent: A measure of “risk” associated with a given radiation dose to a person.
  Rem or mrem, Sievert or mSv
Notes: In order to communicate effectively about the hazards of radiation, several basic quantities commonly used to describe a radiation environment must be understood.
The first and oldest expression of a radiation field is exposure, and is used strictly to quantify the amount of ionization which takes place in air from x-ray or gamma radiation. Exposures are typically expressed in units of the Roentgen (R), or milliRoentgen (mR = 1/1000 of an R). The term is losing popularity, but medical x-rays are still commonly expressed in terms of exposure measurements.
The most widely used expression of radiation effect is dose. A given dose of radiation represents the energy imparted to matter per unit unit mass of the irradiated material. It is commonly expressed in rads, where 1 rad = 0.01 joules per kg of material, or Gray (Gy), defined as 1 joule per kilogram.
The dose equivalent is a quantity used for radiation protection purposes, that expresses on a common scale for all radiations the hazard or "risk" associated with a given dose of radiation. The dose equivalent is calculated from the dose multiplied by a "quality factor" which is specific for the type of radiation involved. For example, alpha radiation is considered a very biologically damaging radiation and as a result has a quality factor of 20 applied to it. In contrast gamma, x-ray and beta radiations are much less biologically damaging and have a quality factor of only 1. The dose equivalent is commonly expressed in rems or sieverts (Sv); 1 rem = 0.01 Sv.

## Slide 26: Activities or Effects of Radiation Dose
Food Irradiation: 100000 rads
Cancer Radiation Therapy: 6000 rads
Lethal WB Dose to 50% of Population: 350 rads
Increase risk of cancer by 1% 12.5 rem
Maximum Annual Occupational Dose: 5 rem
Average Annual U.S. Population Dose: 360 mrem
Average Dose from Radon per year: 200 mrem
Annual Dose Limit for General Population: 100 mrem
Dose from a skull x-ray: 8 mrem
Dose from round-trip flight LA to NY: 2 mrem
Notes: This table is intended to allow some perspective on the effect of various doses and dose equivalents. At the high end, thousands of rads of radiation are used to sterilize food and medical equipment. These doses are intended to kill the microorganisms which exist in food. Similarly, doses up to several thousand rads can be applied over a weeks time to a cancerous tumor in an effort to kill the cancerous cells.
If a sample of the population were exposed to 350 rads, it is predicted that about 50% of the population would be killed from the lethal effects of the radiation dose.
Below a dose 50 rads, it is predicted that little if any immediate effects on the exposed population would be seen. Below this level, radiation doses are thought only to increase the "risks" of health effects like cancer and genetic effects. For a dose equivalent of 12.5 rem, it is thought that one has an increased risk of cancer of one percent.
The remaining numbers reflect maximum annual dose limits for occupationally exposed workers and for the general public, as well as typical annual background radiation doses.
The last values reflect the dose equivalent from a skull x-ray and round-trip flight from LA to NY.

## Slide 27: Biological Effects of Ionizing Radiation Known to Occur at High Doses
Non-Stochastic Effects: A health effect where the severity of the effect increases with dose:
  Cataracts
  Sterility
  Loss of Hair (Epilation)
  Skin Reddening (Erythema)
  Acute Radiation Syndrome
  Death
Stochastic Effects: A health effect where the “risk” of occurrence increases with dose:
  Cancer
  Genetic Effects
Notes: Radiation effects are loosely broken into two broad categories, non-stochastic and stochastic effects.
Non-stochastic effects are associated with large radiation doses received in a short period of time. These effects are only considered to occur after a certain threshold dose has been exceeded and the severity of the effect is considered proportional to the dose above this threshold. The most common non-stochastic effects as observed in the Hiroshima and Nagasaki bomb victims and from the victims of Chernobyl include the acute radiation syndrome, skin reddening and "burns", and cataracts.
Stochastic radiation effects are associated with low doses of radiation received over a long period of time, so called chronic radiation exposure. Stochastic means random in nature, hence stochastic effects are thought to become more probable the higher radiation dose. The effect which causes the most concern is radiation induced cancer. A second effect of much lower probability is genetic effects, or the altering of either the sperm or eggs in a parent which then results in a mutation in their children. Stochastic radiation effects are the largest concern for most radiation protection activities.

## Slide 28: Cancer and Cancer Risk
Each year 1,000,000 cancers are diagnosed in the U.S.
Cancer is the second leading cause of death in the U.S. Approximately 1 in 6 will die of cancer.
Radiation exposure does not cause unique forms of cancer.
The risk of cancer from radiation exposure is assumed to be linear with dose (ICRP 60)
It is estimated that if 1,000,000 people were each exposed to 1 rem, there will be:
    100 additional leukemia cases
    700 additional other cancers (BEIR V)
Notes: As discussed, cancer is the most significant concern from radiation exposure. The normal incidence of cancer results in it being the second leading cause of death in the US, with between one in five and one in six dying from cancer.
Because radiation induced cancer is not unique or different from any other type of cancer, it is impossibly to tell if a given person has developed cancer from radiation or from any other potential cause including genetic or other environmental factors.
Based on data from the survivors of Hiroshima and Nagasaki, and from other studies of people who have received large doses of radiation, the National Academy of Sciences has proposed that if 1,000,000 people were each exposed to one rem, there would be approximately 800 additional cancer deaths in this population. Since up to 200,000 of these people will normally develop cancer, this suggests that the "risk" of cancer from typical annual radiation doses and occupational exposures is very low.
Despite this low risk, the International Commission on Radiological Protection (ICRP) has recommended that persons maintain there exposures as low as possible to minimize their risk of radiation induced cancer. This recommendation is based on their belief that the risk of radiation induced cancer is proportional with the dose one receives. Thus the lower a persons dose, the lower the probability of getting cancer from radiation.

## Slide 29: Radiation and Risk Perceptions and Reality
Nuclear Power
Motor Vehicles
Handguns
Smoking
Motorcycles
Alcoholic Beverages
Private Aviation
Police Work
Pesticides
Surgery
Fire Fighting
Large Construction
Hunting
Spray Cans
Mountain Climbing
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Public
Notes: Risk is defined as an exposure to the chance of injury or loss, a hazardous or dangerous chance. It is generally accepted that there are numerous risks in modern society ranging from the risk of getting hit by a car when crossing a street to contracting AIDS from having unprotected sex. What is less well understood are the perceptual factors which we apply when deciding if something is risky or not, and what risks we should take and which to avoid. Characteristically, we perceive something to be of low risk if we can control it, observe it, understand its nature or if the effect is of low consequence. In contrast, high risks are perceived with events we can’t control, cannot observe, are not readily understood or if the consequences are severe. Nuclear technology, and more specifically nuclear power is typically perceived by the public as high risk because its nature meets the latter set of criteria.
The following four slides compare how the public ranks the risk of dying from various activities and technologies. The latter two slides present expert opinions on how these activities should be ranked. Note that the experts ranking closely matches known fatality statistics, and that the experts consider nuclear technology safe as compared to the general public.
Statistics from Science86 magazine. Oct 85, Vol 6 No 8, pg 40.

## Slide 30: Radiation and Risk: Perceptions and Reality
Bicycles
Commercial Aviation
Electric Power
Swimming
Contraceptives
Skiing
X-Rays
High School and College Football
Railroads
Food Preservatives
Food Coloring
Power Mowers
Prescription Antibiotics
Home Appliances
Vaccinations
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
Public

## Slide 31: Radiation and Risk: Perceptions and Reality
Nuclear Power
Motor Vehicles
Handguns
Smoking
Motorcycles
Alcoholic Beverages
Private Aviation
Police Work
Pesticides
Surgery
Fire Fighting
Large Construction
Hunting
Spray Cans
Mountain Climbing
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Public
20
1
4
2
6
3
12
17
8
5
18
13
23
26
29
Experts

## Slide 32: Radiation and Risk: Perceptions and Reality
Bicycles
Commercial Aviation
Electric Power
Swimming
Contraceptives
Skiing
X-Rays
High School and College Football
Railroads
Food Preservatives
Food Coloring
Power Mowers
Prescription Antibiotics
Home Appliances
Vaccinations
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
Public
15
16
9
10
11
30
7
27
19
14
21
28
24
22
25
Experts

## Slide 33: Radiation and Risk: Days of Life Lost from Various Risks
Being an unmarried male
Smoking cigarettes and male
Heart disease
Being an unmarried female
Being 30 percent overweight
Cancer
Being 20 percent overweight
Having only an 8th grade education
Smoking and being female
Being poor
Stroke
Having a dangerous job
Driving a car
Pneumonia, Flu
Alcohol
Accidents in the home
Suicide
Diabetes
3,500
2,250
2,100
1,600
1,300
980
900
850
800
700
520
300
207
141
130
95
95
95
Notes: A measure of risk for some activities, events and lifestyles is the loss of life expected for that risk. The following two slides present various risks and activities with the loss of life in days expected from them.
It is important to note that radiation and radiation related activities have a relatively low impact on life expectancy.

## Slide 34: Radiation and Risk: Days of Life Lost from Various Risks
Being Murdered
Having an average risk job
Drowning
Having a job with radiation exposure
Falls
Walking down the street
Having a safe job
Fires and burns
Using illegal drugs
Poisoning
Suffocation
Natural Radiation
Medical X-Rays
Coffee
Oral contraceptives
Riding a bike
Drinking Diet Sodas
Radiation from Nuclear Industry
90
74
41
40
39
37
30
27
18
17
13
8
6
6
5
5
2
0.02

## Slide 35: Radiation and Risk: Activities which increase risk by 1 in a Million
Smoking 1.4 Cigarettes
Drinking 0.5 liter of wine
Spending 1 hour in a coal mine
Spending 3 hours in a coal mine
Living two days in Boston or New York
Traveling 10 miles by bicycle
Traveling 150 miles by car
Flying 1000 miles by jet
Flying 6000 miles by jet
Living two months in Denver
Living two months in brick building
One chest x-ray
Eating 40 Tablespoons of peanut butter
Living 5 years at site boundary of
a nuclear plant
Eating 100 charcoal -broiled steaks
Living within 5 miles of a nuclear
reactor for 50 years
Cancer, heart disease
Cirrhosis of the liver
Black lung disease
Accident
Air Pollution
Accident
Accident
Accident
Cancer caused by cosmic radiation
Cancer caused by cosmic radiation
Cancer caused by natural radiation
Cancer caused by radiation
Liver cancer caused by aflatoxin B
Cancer caused by radiation
Cancer from benzopyrene
Cancer caused by accidental radiation
release
Notes: A common expression to indicate that something is very unlikely is to say that the odds of it happening are one in a million. This slide summarizes several activities, events, and risks which are estimated to increase your risk of dying by one in a million. The cause of death is noted in the second column.

## Slide 36: Nuclear Power
Notes: Nuclear Power in the U.S. provides approximately 20% of the electricity needs of the country, with up to 50% of the energy demands in New England and parts of the midwest. France is the largest user of nuclear power in the world, with over 73% of the countries needs provided by nuclear energy.
There are 71 operating pressurized water reactors and 37 operating boiling water reactors in the USA. Each generates about 1000 megawatts of electricity when operating. In the world their are over 500 power reactors of different designs and powers.
In addition to power reactors, there are 35 university research reactors and a number of other Department of Energy reactor facilities throughout the country . These reactors do not provide power, but are used either for education and research, or support of the U.S. weapons program, respectively.
Handout simulated uranium fuel pellet samples.

## Slide 37
Fission
Uranium-235
Plutonium-239
Neutron
10n
10n
10n
Strontium-90
Xenon-144
Notes: Fission is a process in which very heavy atoms, such as uranium and plutonium, after “absorbing” a neutron becomes so unstable that they literally split into two pieces accompanied by a large release of energy.
The energy released per fission is approximately 200 megaelectronvolts, equivalent to about 3.2x10-11 J of energy, (a very small number). However this energy release is over two million times larger than that given up in most chemical reactions, for example in the burning of coal.
If 1 gm of uranium-235 were to completely fission, it would require burning approximately 4900 pounds of coal to result in an equivalent energy release.
To generate 1 J of energy 3.1x1010 fissions must occur. Most modern reactors operate at about 3800 megawatts of power which is 3,800,000,000 joules per second. To create this power level, 1.18x1020 fissions must occur in the reactor each second.

## Slide 38
Fission Chain Reactions
Neutron
Uranium-235
Plutonium-239
10n
Notes: A chain reaction is the process where neutrons produced from fission go on to cause fissions in surrounding uranium atoms. Some of the neutrons produced will escape from the reactor core, while others will interact with other core materials other than fuel. These neutrons are “lost” and reduce the chain reaction process.
If the number of fissions in the first generation equal the number of fissions in a second generation, the chain reaction is said to be “critical”.
If the number of fissions is increasing between generations, the reaction is said to be supercritical, and the power level of the reactor will increase exponentially.
If the number of fissions in decreasing between generations, the reaction is “subcritical” and the power will drop away dramatically.
A nuclear reactor is operated so it is “critical” at some established power level, usually about 3800 megawatts thermal. To increase power the reactor is temporarily made supercritical, while to decrease power the reactor is made temporarily subcritical.

## Slide 39: Basic Design of a Reactor Core

## Slide 40: Pressurized Water Reactor
Control
Rods
Steam
Generator
Turbine
Generator
Pump
Pump
Pump
Reactor
Vessel
Core
Condensor
Cooling Water
Primary Containment
Notes: A pressurized water reactor has two separate “loops” through which cooling water flows. The primary loop is fully located within the containment structure and uses liquid water under pressure to remove heat from the core as well as act as a moderator for fission neutrons. (A moderator is a substance which slows down high energy neutrons so that they can cause fission more easily). Water passes through the core from the bottom, is heated as it passes by the fuel and passes out through the top section of of the pressure vessel to the steam generators. After some of its energy is transferred to the secondary loop via the steam generators, the primary “coolant” is routed back to the pressure vessel through a large pump.
The heat transferred to the secondary loop via the steam generators produces steam which is routed to turbines which then produce electricity. The “spent” steam is then condensed and routed back through the steam generators.
Typical Characteristics of Pressurized Water Reactors:
  Power thermal: 3800 MW
  Power electric: 1300 MW
  Core: 4.17 m high, by 3.37 m diameter
  Fuel Rod OD: 9.5 mm
  Fuel Pellet Diameter: 8.19 mm
  Rods per Fuel Assembly: 264 (17 x 17)
  Fuel Assemblies in Core: 193
  Fuel Loading: UO2: 115x103 kg (2.54x105 lb)
  Average Fuel Enrichment: 3.3% U-235
  Control Rod Clusters: 20 - 24 rods per assembly, Ag-In-Cd
  Control Assemblies: 61 full length, 8 part length

## Slide 41: Boiling Water Reactor
Turbine
Generator
Pump
Pump
Reactor
Vessel
Condensor
Cooling Water
Primary Containment
Control
Rods
Core
Pump
Jet
Pump
Notes: A boiling water reactor consists of a single loop through which water flows acting as both coolant and moderator. Water enters the reactor vessel from the side and is then forced below the core via jet pumps. Special recirculation pumps are located on the side of the core to move the coolant through the jet pumps to the area below the core. The water then flows up through the core where it is transformed into steam. The steam is “dried” above the reactor core and then routed directly to the steam turbines outside containment where electricity is produced. The “spent” steam is then condensed and routed back to the reactor vessel.
The coolant loop features special isolation valves to prevent radioactivity from leaving the containment area if there is an accident in the core.
Typical Characteristics of Boiling Water Reactors:
  Power thermal: 3830 MW
  Power electric: 1330 MW
  Core: 3.76 m high, by 4.8 m diameter
  Fuel Rod OD: 12.52 mm
  Fuel Pellet Diameter: 10.57 mm
  Rods per Fuel Assembly: 62 (8x8)
  Fuel Assemblies in Core: 784
  Fuel Loading: UO2: 168x103 kg (3.69x105 lb)
  Average Fuel Enrichment: 2.6% U-235
  Moveable Cruciform Element: 193, Boron-Carbide

## Slide 42: Barriers Against Release of Radiation
Core
Steel
Containment
Concrete
Shield
Building
Fuel Pellets
Fuel Rods
Steel
Pressure Vessel
Notes: To ensure that radioactive materials used in a nuclear reactor are maintained in the reactor system, they are enclosed by a system of physical barriers. The fuel pellets, fuel rods, steel reactor pressure vessel, inner containment structure and reinforced concrete containment building comprise the multilayer defense-in-depth design.

## Slide 43: Source Energy Equivalents
15 Barrels of oil
5 Tons of coal
12 1/2 Tons of wood
85,000 cu ft of natural gas
A crayon* (without the tip) is about the size of five
uranium fuel
pellets stacked together
Five uranium
fuel pellets ..
have as much energy
available in todays nuclear power plants as...
* Crayons are not radioactive nor are they used as nuclear fuel

## Slide 44: IONIZING RADIATION
School Presentation
Notes: 1.Introduce self
2.Hand out copies of viewgraphs , LLNL 1994 Radiation Dose to Employees graph and other appropriate material
3.Ask to sign the roster
4.Describe why the class is offered and who should be here.
5.Explain that a test will be given at the end
6.Discuss the fact that LLNL is a “Nuclear Facility” and has Special Nuclear Material on-site (define what this is)

## Slide 45: What Will You Learn Today?
Identify natural background and manufactured sources of radiation.
Learn how radiation affects living things.
Learn how radiation is detected using radiation survey meters
Notes: 1.Go through the objectives and note that the objectives will be what the test will cover.

## Slide 46
The three basic particles of the atom are PROTONS, NEUTRONS AND ELECTRONS
There are stable and unstable atoms

## Slide 47
UNSTABLE atoms emit energy

## Slide 48: Non-Ionizing Radiation Does not have enough energy to remove electrons from surrounding atoms
Notes: 1.Discuss what non-ionizing radiation is and explain our current state of knowledge on health effects associated with non-ionizing radiation.
2.Discuss briefly the fact that we have lasers on-site that are sources of non-ionizing radiation.

## Slide 49: Ionizing Radiation - can deposit energy in neighboring atoms resulting in the removal of electrons.
Notes: 1.Briefly describe what a alpha, beta, gamma, x ray and neutron is and give example of these found at LLNL.

## Slide 50
Alpha Radiation is only a hazard when inside your body (internal hazard)
Your skin will stop it
can’t penetrate skin
internal hazard
stopped by paper
found in soil, radon and other radioactive materials

## Slide 51
Beta Radiation is a Skin, Eye and Internal Hazard
skin, eye and internal hazard
stopped by plastic
found in natural food, air and water

## Slide 52
stopped by lead
naturally present in soil and cosmic radiation
found in medical uses
X and gamma radiation are penetrating
radiation and an EXTERNAL HAZARD.

## Slide 53
Neutron particles have no charge and can penetrate deep into the body

## Slide 54: Radiation Versus Radioactive Contamination
Radiation is particles or waves of energy emitted from unstable atoms.
Radioactive Contamination is radioactive material usually in any location you do not want it.
Notes: 1.Give practical examples of radiation and radioactive contamination.
i.e. - x ray exposure does not result in contamination
- a spill of a liquid radioactive source can result in fixed or loose contamination

## Slide 55: Background and Manufactured Radiation In the U.S. Contributes 360 mrem per Year
cosmic - 28
diet - 40
terrestrial - 28
radon - 200
Notes: 1.Explain where the sources of background radiation come from.
2.Discuss types of medical exposures.

## Slide 56
<footer>
<date/time>
mrem
Manufactured sources of radiation contribute an average of 60 mrem/year
cigarette smoking - 1300 mrem
round trip US by air
5 mrem per trip
building materials - 3.6
fallout < 1
smoke detectors - 0.0001
medical - 53
mrem
mrem
mrem
Notes: 1.Explain briefly why these manufactured sources are radioactive and how you get dose from them.

## Slide 57: Biological Effects of Radiation
Early scientists determined that radiation was a useful tool but it could hurt you.
Radiation can cause burns and cellular damage.
Notes: 1.Explain how the early scientist’s that discovered and worked with radiation experienced burns and illness from their exposures.
2. Explain why cancer cells are more sensitive to radiation therefore it is an effective treatment for tumors.

## Slide 58: Biological Effects of Radiation
The principle hazard from radiation exposure is an increase in the risk of cancer induction.
Notes: 1.Explain why we believe cancer has no threshold response and why we believe there is a small risk of cancer at any level of radiation exposure.
2.Discuss the current risk of dying from cancer in the U.S.(20%)
3.Define heritable effects and discuss the fact that they have been demonstrated in plants and cells but not in humans.

## Slide 59
SIGNS ARE REQUIRED TO NOTIFY EVERYONE OF THE PRESENCE OF RADIATION

## Slide 60: MONITORING RADIATION EXPOSURE
Radiation dosimeters measures radiation dose to people.
Notes: 1. See page 6-7 of Radiation Safety booklet for more details.
2. Discuss how to properly care and use the badge and what it detects.

## Slide 61: Minimize Dose By Good Practices
TIME - reduce time of exposure
DISTANCE - increase distance
SHIELDING - use shielding
Notes: 1. Demonstrate with a meter time, distance and shielding principles.

## Slide 62
Alpha Survey Meter
Radiation is detected with survey meters
Beta, Gamma & X-ray Survey Meter

## Slide 63: Radiation and Life
Radon
X-Rays
Consumer
Products
Nuclear
Power
Radioactive
Waste
Nuclear Medicine
Solar Radiation
Cosmic Rays
Terrestrial
Radiation
Food &
Drink
Milk
Each
Other
  
Notes: We are all exposed to radiation each day of our life.
Natural sources of this exposure include radiation emitted by the sun and from the universe as a whole, radiation emitted from naturally occurring radionuclides in the soil and building materials, radiation from radionuclides produced by cosmic radiation in the atmosphere, and radiation dose we receive internally from radon and from small amounts of radioactivity in the food and water we drink.
Man-made sources of radiation which add to this dose include dose we receive from consumer products and from the medical use of radiation, radiation from the nuclear fuel cycle, from the fall-out of nuclear weapons tests in the 1950s and 60s, and from occupational exposure to radiation.
Finally, since we are all “slightly” radioactive from naturally occurring radioactive materials in our body, we receive a small radiation dose from just being near another person.
Slides of solar radiation and earth
Demonstrate brazil nuts, bananas, cigarettes

## Slide 64: Contribution of Various Sources of Radiation to Average Annual Dose
Radon 55%
Cosmic
8%
Terrestrial
8%
Internal
11%
Medical
X-Rays
11%
Nuclear
Medicine
4%
Consumer
Products (3%)
Other (<1%)
Occupational 0.3%
Fallout <0.3%
Nuclear Fuel
Cycle 0.1%
Miscellaneous 0.1%
Notes: The National Council on Radiation Protection and Measurements (1987) attributes about 55% of our annual radiation dose. Of least significance is exposures from the nuclear fuel cycle, fall-out and occupational exposures.

## Slide 65: Average Annual Effective Dose in U.S. Population, (1980-82)
Natural Sources
  Radon
  Cosmic
  Cosmogenic
  Terrestrial
  In the Body
Occupational
Nuclear Fuel Cycle
Consumer Products
  Tobacco
  Other
Medical
  Diagnostic X Rays
  Nuclear Medicine
200 mrem
27 mrem
10 mrem
28 mrem
39 mrem
0.9 mrem
0.05 mrem
----
5 - 13 mrem
39 mrem
14 mrem
Total Annual
Dose = 360 mrem
Upto 16 rem to
Bronchial epithelium
(Lung lining)
Notes: The National Council on Radiation Protection and Measurement has estimated that the average annual effective dose to general public as being about 360 mrem, with the majority of this dose resulting from radon and its decay products.
For those individuals who smoke, there is an additional radiation exposure to the lungs from the naturally occurring radionuclides in tobacco products. It is estimated that the average dose to a small portion of the lung lining is about 16000 mrem.

## Slide 66: Early Uses of Radioactivity
Radiation Therapy
Welsbach Thorium Gas Mantles
Uranium Ceramic Glazes
Anna Glass (Uranium Nitrate)
Luminous Dials (Radium)
Patent Radium Therapies
  Radithor
  Radium Poultices
Radon Spas and Mineral Waters
  Revigator
  Thoronator
Notes: At the turn of the century, radiation was the new fascination of science and society. Within a year following the purification of radium by the Curies in 1898, Europium physicians were experimenting with its use as a treatment for cancer. By 1900, similar investigations were being carried out in the USA. By 1920, “Curie-Therapy” was well respective as an adjuvant to surgery.
During this period, it was discovered that mineral waters from many of the great resort spas in Europe and the U.S. were abnormally high in their concentrations of the radioelements. These waters had long been respected for their curative properties and the new finding of radioactivity was attributed by many as the reason for there beneficial effects. This lead to the medical fadism of the time that drinking waters with high radon concentrations, or ingesting radium solutions was an energy tonic and a panacea for a variety of ills including goiter, arthritis, and impotence.
The end of the era of patent radioactive medicines occurred in the late 1920s, when a number of young women who had worked as radium dial painters developed bone cancer. These women would apply a luminous mixture of phosphorescent paint and radium to clock faces by hand painting the numbers and dials. By using there lips to get a very fine point on there brushes, they slowly ingested large quantities of radium which then lead to aplastic anemia and cancer in many of the workers.
Other applications of radioactive material included using thorium oxide in Welsbach gas mantles to increase the luminosity of gaslights during the Victorian. FInally uranium was used to provide a vivid orange color on ceramic glazes and a bright yellow-green coloring in glass.
Demonstrate Fiestaware, Vaseline Glass and Radium Dial Clocks.

## Slide 67: Modern Uses of Small Amounts of Radioactive Material or Radiation
Ophthalmic Glass
Aerosol (Smoke) Detectors
Airport Inspection Systems
Lantern Mantles
Fluorescent Lamp Starters
Welding Rods
Fluid Guages
Check Sources
Uranium Counterweights and Shielding
Notes: Today radioactivity is commonly used in many consumer products and industrial applications because of the unique physical properties of radiation, or for the special chemical properties of the radioactive element.
The most familiar use of a radioactive material in consumer products is the use of americium-241 in the household smoke detector. Americium-241 is an alpha emitter that ionizes the air between two electrodes, thereby allowing an electric current to flow across the air gap under the influence of a small potential. When smoke enters the air gap, the flow of current between the electrodes is decreased which triggers an alarm.
Other products where the ionizing properties of radiation are used include fluorescent lamp starters, fluid guages and check sources.
An example of a radioactive material used for its chemical properties is the use of thorium in optical glass, lantern mantles and welding rods. In each case, thorium's chemical properties are required to improve the properties of these manufactured items.
Uranium is material that is used for its physical properties. Uranium is the heaviest material commonly available, but it is also radioactive. Because of its density, it is used for shielding of radiation sources and as a counterweight in aircraft design. It is also used in armor piecing munitions for the military.
Demonstrate smoke detector and compact fluorescent light bulb.

## Slide 68: Modern Uses of Large Amounts of Radioactive Materials or Radiation
Nuclear Power
Nuclear Propulsion
Nuclear Weapons
Food and Medical Supply Irradiation
Industrial Radiography
Scientific Research
Medical X-Rays
Nuclear Medicine Services
Notes: Today, the use of radiation and radioactivity is integral to life in the twentieth century. From nuclear power to nuclear medicine, radiation is critical to providing electricity, safeguarding our nation, developing new technologies, and evaluating our health. The following slides demonstrate some of the applications of radiation in modern society.
Nuclear related industries employ several million people throughout the nation. These workers receive occupational radiation doses which average about 110 mrem per year as part of the performance of their jobs. It is important to note that these doses are strictly controlled by state and federal government agencies, like the Nuclear Regulatory Commission, to minimize the health consequences from these exposures. The current annual dose limits for persons employed in the nuclear power industry and other related industries is 5000 mrem per year.

## Slide 69
RADON
and
Life

## Slide 70: Uranium Decay Series
<footer>
<date/time>
Uranium-238
4.5E9 y
Protactinium-234m
1.2 m
Uranium-234
2.5E5 y
Thorium-234
24 d
Thorium-230
7.5E4 y
Radium-226
1600 y
Radon-222
3.825 d
Lead-214
27 m (RaB)
Polonium-218
3.1 m (RaA)
Polonium-214
163.7 us (RaC’)
Bismuth-210
5 d (RaE)
Bismuth-214
19.9 m (RaC)
Lead-210
22.3 y (RaD)
Lead-206
Stable
Polonium-210
138 d (RaF)
Beta Decay
Alpha Decay
Notes: Radon is a noble gas that is produced by the decay of uranium, which occurs naturally in the soil. Radon itself is relatively harmless. As an inert gas, it is simply breathed into the lungs and then exhaled. Radon however decays into radioactive elements which are solids. These products if inhaled, can be retained within the lungs and can contribute significant doses to the lungs. They are often referred to as “radon daughters or “radon progeny”.
To illustrate how common uranium, radium and radon are in the environment, there is about 30 tons of uranium in the first 5 feet of soil covering a surface area of 1 square mile. Within this same volume there is about 10 Curies of radium. This concentration results in about 2 microcuries of radon per cubic yard of soil, which releases about 0.1 microcurie of radon into the air each day.
Demonstration of uraninite specimen.

## Slide 71: Uranium Decay Series
<footer>
<date/time>
Uranium-238
4.5E9 y
Radium-226
1600 y
Radon-222
3.825 d
Lead-214
27 m (RaB)
Polonium-218
3.1 m (RaA)
Polonium-214
163.7 us (RaC’)
Bismuth-214
19.9 m (RaC)
Lead-210
22.3 y (RaD)
Notes: Radon is a noble gas that is produced by the decay of uranium, which occurs naturally in the soil. Radon itself is relatively harmless. As an inert gas, it is simply breathed into the lungs and then exhaled. Radon however decays into radioactive elements which are solids. These products if inhaled, can be retained within the lungs and can contribute significant doses to the lungs. They are often referred to as “radon daughters or “radon progeny”.
To illustrate how common uranium, radium and radon are in the environment, there is about 30 tons of uranium in the first 5 feet of soil covering a surface area of 1 square mile. Within this same volume there is about 10 Curies of radium. This concentration results in about 2 microcuries of radon per cubic yard of soil, which releases about 0.1 microcurie of radon into the air each day.
Demonstration of uraninite specimen.

## Slide 72: How Does Radon Get in the Home?
1. Cracks in Solid Floors
2. Construction Joints
3. Cracks in Walls
4. Gaps in Floors
5. Gaps around Pipes
6. Cavities in Walls
7. The Water Supply
3.
4.
1.
2.
7.
6.
5.
Notes: Radon has a half-life 3.8 days. As a result, it is around long enough so that once produced in the soil, it can diffuse into basements and the living spaces of homes where it then becomes of source of solid radioactive decay products.
Since the first several radioactive daughters of radon all have short half-lives, they quickly decay. If inhaled, they result in a dose to the lung.
Radon enters the home through any of the seven mechanisms listed above. With respect to the water supply, it is estimated that a concentration of 10,000 pCi/liter of water results in an increase of indoor air radon levels of 1 pCi/liter.

## Slide 73: How is Radon Detected
Charcoal Canisters
Alpha Track Detectors
Electret Monitors
Radon Sniffers
Notes: There are four methods commonly used to measure radon in the home.
a. The first is based on the use of a small charcoal canister in which radon gas is adsorbed. After opening the canister in the area to be assessed, the canister is sent to a laboratory for analysis. This is done by determining the concentrations of the radon decay products in the canister, and extrapolating back to the concentration of radon in the home.
b. The second method uses either a small piece of radiosensitive film or plastic to detect the presence of alpha radiation caused by radon decay. Radon gas which enters the alpha-track detector decays and causes minute tracks to form on the film or plastic. Chemical development of the film or chemical etching of the plastic makes these tracks observable through low magnification. The tracks can then be counted and related to the radon level in the structure.
c. A third approach uses charged teflon disks called “electrets” which are exposed in a room to be monitored. As radon decays, the disk is slowly discharged by the negative ions formed when the alpha radiation ionizes the air around the electret. By measuring the decrease in charge between the start and end of monitoring, an assessment of the radon concentration can be made.
d. Finally, radon sniffers are highly sensitive (and expensive) radon detecting instruments which assess radon levels immediately through sniffing the air and measuring the radon concentration directly.
Demonstrate various sampling devices.

## Slide 74: Cancer Death Estimates for Radon
Deaths
per
Year
Between 7,000 and
30,000 Deaths
Notes: The following three slides are taken from the EPA Citizens Guide to Radon, Second Edition (Air and Radiation ANR-464) 402-K92-001.

## Slide 75: Radon Risk If You Smoke...
20 pCi/l
10 pCi/l
8 pCi/l
4 pCi/l
2 pCi/l
1.3 pCi/l
0.4 pCi/l
About 135 people could get lung cancer
About 71 people could get lung cancer
About 57 people could get lung cancer
About 29 people could get lung cancer
About 15 people could get lung cancer
About 9 people could get lung cancer About 3 people could get lung cancer
100 times the risk of drowning
100 times the risk of dying in a home fire
100 times the risk of dying in an air plane crash
2 times the risk of dying in a car crash (Average indoor radon level)
(Average outdoor radon level)
Radon
Level
If 1,000 people who smoked were exposed to this level over their lifetime..
The risk of cancer exposure compares to..
Notes: Discussion of relative risk for smokers, as proposed by EPA

## Slide 76: Radon Risk If You’ve Never Smoked
20 pCi/l
10 pCi/l
8 pCi/l
4 pCi/l
2 pCi/l
1.3 pCi/l
0.4 pCi/l
About 8 people could get lung cancer
About 4 people could get lung cancer
About 3 people could get lung cancer
About 2 people could get lung cancer
About 1 person could get lung cancer
Less than 1person could get lung cancer Less than 1 person could get lung cancer
Risk of being killed in a violent crime
10 times the risk of dying an an airplane crash
The risk of drowning
The risk of dying in a home fire (Average indoor radon level)
(Average outdoor radon level)
Radon
Level
If 1,000 people who smoked were exposed to this level over their lifetime..
The risk of cancer exposure compares to..
Notes: Discussion of relative risk for non-smokers as proposed by EPA.
Demonstration od air sample collected in classroom or vicinity.

## Slide 77: Radiation and Risk
How Risky is it Really??

## Slide 78: Years from Your Life

## Slide 79: Days from Your Life

## Slide 80: Hours from Your Life