| NEW JERSEY DIVISION OF GAMING ENFORCEMENT TECHNICAL SERVICES BUREAU |
| --- |
|  | OSI #: |  |
| CASINO: |  |  |
| SCHEDULED INSPECTION DATE: |  | TIME: |  |
| DGE SLOT MACHINE INSPECTION CHECKLIST |

| Breakdown of Machines to be Inspected: |
| --- |
| MANUFACTURERS | IGT | Bally | Sigma | WMS | Atronics | VLC | Anchor | Other |
| # of Machines |  |  |  |  |  |  |  |  |
| Type of Inspection * |  |  |  |  |  |  |  |  |

| * | N = New | P = Percentage | D = Denomination | MO = Modification | RV = Revoked Program Update | B = Seal Break | S = Program Seal | O = Other |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

##### GENERAL OPERATION

|  |  | Casino |  | DGE |  | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | OSI papers reviewed for accuracy (Correct Serial Nos., etc.) |  |  |  |  |  |
| 2. | List all programs to be sealed on OSI document including board position number |  |  |  |  |  |
| 3. | Coupon acceptance: record GMU EPROM on OSI |  |  |  |  |  |
| 4. | Correct asset number and location |  |  |  |  |  |
| 5. | Cabinet void of holes or loose components |  |  |  |  |  |
| 6. | Correct serial # on MPU board, hard drive, CD & cabinet |  |  |  |  |  |
| 7. | Reels sequentially numbered |  |  |  |  |  |
| 8. | Correct denomination tested with coins |  |  |  |  |  |
| 9. | Coin acceptor contains correct sample coin |  |  |  |  |  |
| 10. | Correct max coin |  |  |  |  |  |
| 11. | All acceptable denominations on validator and log book |  |  |  |  |  |
| 12. | All DIP switches set correctly |  |  |  |  |  |
| 13. | All lights, sound and switches operable |  |  |  |  |  |
| 14. | Correct payable glass and/or screen and tower light color |  |  |  |  |  |
| 15. | Complete paytable on glass and/or screen |  |  |  |  |  |
| 16. | Game rejects coins beyond max coin |  |  |  |  |  |
| 17. | Game rejects other denominations |  |  |  |  |  |
| 18. | Hopper test satisfactory |  |  |  |  |  |
| 19. | MEAL Book |  |  |  |  |  |
| 20. | Locks installed, i.e., doors’ locks, bill validator |  |  |  |  |  |

| TEST OPTIONS |
| --- |
|  |  | Casino |  | DGE |  | Notes |
| 21. | EPROM and/or paytable test correct |  |  |  |  |  |
| 22. | Denomination correct and not changeable when bill validator is enabled |  |  |  |  |  |
| 23. | Hopper and bill lockup amounts comply with IRS rules and agree with award glass. |  |  |  |  |  |
| 24. | Any partial pay accurately described on glass |  |  |  |  |  |
| 25. | Validator settings match posted denomination |  |  |  |  |  |
| 26. | Game Rules and appropriate disclaimers on award glass |  |  |  |  |  |
| EPROM SEALS, MAIN AND/OR SECONDARY CHARGES |
| 27. | EPROM Seals in Place |  |  |  |  |  |
| 28. | Serial NO.’s match OSI |  |  |  |  |  |
| 29. | EPT Set OFF or ON (Circle One) |  |  |  |  |  |
| 30. | Game Recovers from Power Down |  |  |  |  |  |
| PROGRESSIVE MACHINES |
| 31. | DGE & CCC Approval Letters & Verify Parameters |  |  |  |  |  |
| 32. | Link Communication with controller |  |  |  |  |  |
| 33. | MEAL Book |  |  |  |  |  |

| Technical Shift Manager or Higher Signature |  |  | Date: |  |  |
| --- | --- | --- | --- | --- | --- |
| Gaming Equipment Specialist Signature |  |  | Date: |  |  |